## Slide 1: Unit 3: Receive Filtering
EL-GY 6013: Digital communications
Prof. Sundeep rangan

## Slide 2: This Unit
Channel coding
Symbol mapping
Coded bits
TX filter DAC
IQ symbols
Analog baseband
Upconversion
Info bits
Passband
Channel
Down-conversion
RX filter and ADC
Sync
Equalization
Symbol demod
Channel decoding
RF

## Slide 3: Learning Objectives
Describe the steps in recovering symbols for a linearly modulated signal
  Determine the matched filter response
Determine MF for known gain and delay in the channel
Compute the effective discrete-time channel given
  Channel response, TX an RX filter
  Time-domain or frequency-domain method
Determine if there is ISI
Compute the frequency response using digital RX filtering and downsampling
Determine specifications on the digital and analog filters

## Slide 4: Outline
Receiver filtering and sampling
Perfect reconstruction with orthonormal modulation
General channels: Time-domain analysis
General channels: Frequency-domain analysis
PSD Analysis
Practical RX filter design
Channel sounding

## Slide 5: Receiver Problem
Transmit steps so far:
  Symbols
  Linearly modulate:
  Baseband equivalent channel
Question at the receiver: Can we recover the transmitted symbols?
Want a mapping that input to samples
Ideally
TX symbols
TX filter
Channel
Receiver
Ideal D/A

## Slide 6: Simple Idea: Sampling
Take samples with an ideal A/D:
This could work: Example
  Suppose (Ideal zero-order-hold D/A)
  (no channel effect)
  Then:
  So,
  Hence, if we sample at exactly the right time, we can recover
TX symbols
TX filter
Channel
Ideal A/D
Ideal D/A

## Slide 7: Problems with Ideal Sampling
Three problems in implementing an ideal A/D
Problem 1: No circuit exactly samples at one instant
  Most circuits integrate over some period
  Ex: Charge fills a capacitor at the input to the A/D
Problem 2: Out-of-band emissions (“blockers”)
  The received signal may contain signals at neighboring frequencies
  Ex: Transmissions in other wireless channels
  The system may not have control over these
  Without filtering, these will be aliased into
Ideal A/D
PSD of
Frequency
0
Desired
Interferer

## Slide 8: Problems with Ideal Sampling
Three problems in implementing an ideal A/D
Problem 3: No noise filtering
  Suppose that in some symbol period:
  “desired signal” + “noise”.
  Noise will appears in any sample.
  But, suppose we average:
  Effective noise is
  This will, in general, have a lower variance
  We will describe this more next unit
Ideal A/D

## Slide 9: Two Step Receiver
Discussion motivates a two step process
Step 1: Receive filter:
  is the RX filter response
Step 2: Sample
Filter is useful to:
  Model imperfections in the sampling
  Filter out blockers. Anti-aliasing
  Average out noise (more on this later)
Analog filter
ADC
RX complex baseband
RX complex symbols

## Slide 10: Outline
Receiver filtering and sampling
Perfect reconstruction with orthonormal modulation
General channels: Time-domain analysis
General channels: Frequency-domain analysis
PSD Analysis
Practical RX filter design
Channel sounding

## Slide 11: End-to-end TX and RX Chain so Far
Steps:
  Impulse D/A:
  TX pulse shape:
  Channel:
  RX filter:
  Sampling A/D:
TX symbols
Ideal A/D
Ideal D/A

## Slide 12: Basic Questions
Under what circumstances can we construct transmitted signals.
That is, how do we select such that ?
We first analyze this for a simple case:
  Orthonormal pulse shapes
  No channel impairments
TX symbols
Ideal A/D
Ideal D/A

## Slide 13: Inner Products and Orthonormal Signals
Let be two complex-valued signals
Definition 1: The inner product of is:
  Here complex-conjugate of
Definition 2: We say are orthogonal if
  We will write this as
Definition 3: The signal energy is
We will discuss this in much more detail in the next unit on signal spaces

## Slide 14: Example Problem
Suppose
  Complex with
Compute
When is ?
Solution:
  Therefore .
  Since

## Slide 15: Orthogonality in Frequency Domain
Sometimes it is more convenient to evaluate inner products in frequency domain
Parseval’s Theorem: Let be any two signals. Then:
This is useful whenever the Fourier transforms are simple to work out.

## Slide 16: Example
Suppose
Compute . When are they orthogonal?
Solution:
  Do this in frequency domain
  From Parseval’s Theorem: Let
  when for some integer

## Slide 17: Orthonormal Signals
Let be a set of signals
  This can be indexed from to as well
Definition: The set is orthonormal if:
  for all (all signals have unit energy)
  for all (different signals are orthogonal)
This generalizes the concept of orthonormal vectors
We will discuss orthonormal sets much more in signal space theory

## Slide 18: Orthonormal Pulses and Matched Filtering
Consider the linear modulation:
Definition 1: We will say that the modulation is orthogonal if is an orthonormal set.
Definition 2: Given any transmit pulse, , the matched filter RX pulse is:
  The pulse that is complex conjugate and flipped in time
  Note that if TX filter is causal, RX filter is anti-causal

## Slide 19: Reconstruction With Orthonormal Pulses
Theorem: Suppose that:
  generates orthonormal pulse at sample rate
  (i.e. so there are no channel impairments)
  (RX uses matched filter)
  Then the receiver will exactly recover the TX samples in that
Theorem answers our question. We can reconstruct the RX samples
  Under several assumptions
TX symbols
Ideal A/D
Ideal D/A

## Slide 20: Proof of Reconstruction Theorem
TX signal is:
Since
RX filtered signal is:
Sampling is:
Now look at convolution:
At :
But is an orthonormal set
So,
Hence:

## Slide 21: “Practical” Orthogonal Pulses
There are two important “practical” orthonormal pulses
Rectangles:
  Orthonormal since and do not overlap when
  Scaling by ensures they are normalized
  This can be achieved (with some scaling) by a zero-order hold ADC
Sinc pulses:
  Use similar frequency domain calculation as before to prove these are orthonormal
  This would arise with ideal filtering at the TX and RX.
  No filter is exactly ideal.
  But, practical filters get quite close to this response.

## Slide 22: Outline
Receiver filtering and sampling
Perfect reconstruction with orthonormal modulation
General channels: Time-domain analysis
General channels: Frequency-domain analysis
PSD Analysis
Practical RX filter design
Channel sounding

## Slide 23: Modeling the End-to-End System
We have seen so far that when:
  Pulse shapes are matched
  Modulation is orthonormal
  No channel impairments
Then:
What happens when these conditions fail?
TX symbols
Ideal A/D
Ideal D/A

## Slide 24: Channel Gain
Consider simple deviation: Channel gain
  Gain can be due to attenuation in wire, for example.
Suppose, as before, that:
  are orthonormal for different
  i.e. matched filter
Then
  Proof on board
  Simply scales symbols.
  Can recover symbols from
But, requires that gain is known. More on this later
Channel gain

## Slide 25: Channel Gain and With Known Delay
Now consider gain and delay
Then,
Suppose gain and delay are known
Use shifted and scaled receive filter
Then:
  Proof on board
RX filter is shifted to delay
  Must know the gain and delay
  Requires synchronization
Channel gain

## Slide 26: Integer Delays
Suppose:
  Delay is an integer multiple of the sample period:
Suppose, as before:
  TX uses orthonormal modulation
  MF receiver (but, not shifted and scaled)
Then:
  Channel delay of Symbol delay of
  Proof on board

## Slide 27: Integer Delays visualized
Suppose TX uses orthonormal modulation and RX uses matched filter
Suppose sample rate is ( Msym/s)
Baseband channel impulse response
Effective discrete-time channel

## Slide 28: General case
Define channel impulse response with filtering
  Represents path from DAC output to ADC input
Theorem: Mapping from to is LTI with impulse response is
Receive symbols will be given by
Ideal A/D
Ideal D/A

## Slide 29: Example 1: Rectangular Pulse
Suppose that
If channel is , what is effective DT channel
Solution:
  Impulse response is
  Impulse response from is
  Then

## Slide 30: Example 2 Illustrated
Channel response with filtering
Effective discrete-time channel:
Plot to right:
  Blue dashed
  : Red stem
When is an integer:
  Single tap
When
  has two taps

## Slide 31: Example 2: Exponential
Suppose that
Baseband channel is:
Find filtered channel response and effective discrete-time response
Solution:
  Take Laplace transform of differential eqn:
  Using inverse Laplace transform: where
  Filtered channel response:
  Discrete-time response:

## Slide 32: Example 2: Exponential Illustrated
Suppose that
Baseband channel is:
From previous slide:
  Filtered channel response:
  Discrete-time response:

## Slide 33: Effective Discrete-Time Channel
Lack of synchronization causes channel of the form
called the effective discrete-time channel
Inter-symbol interference:
  Whenever for
  Other symbols interfere with one another
ISI occurs for many reasons:
  Lack of synchronization
  Channel impairments

## Slide 34: ISI and Equalization
Effective discrete-time channel is:
System has inter-symbol interference (ISI):
  Multiple symbols effect
The receiver must undo this ISI.
This process is called equalization
We will discuss this later.

## Slide 35: Outline
Receiver filtering and sampling
Perfect reconstruction with orthonormal modulation
General channels: Time-domain analysis
General channels: Frequency-domain analysis
PSD Analysis
Practical RX filter design
Channel sounding

## Slide 36: Digital Channel Frequency Response
We saw that effective digital channel from is:
Question: What is the frequency response?
Ideal A/D
Ideal D/A

## Slide 37: Frequency Response of DT Filter
Fact from signals and systems: If
Shifted copies of
Continuous frequency mapped to DT frequency
Can obtain coefficients from inverse DTFT:

## Slide 38: Computing Effective DT Frequency Response Summary
Compute frequency response of channel with filtering
Effective DT channel response is:
  Scale vertically by
  Map continuous-time frequency to
  Create shifted versions every
  Shifted versions may overlap if there is aliasing

## Slide 39: Bandlimited Channel
Suppose one of or bandlimited to ,
Effective discrete-time channel reduces to
  for
If TX and RX filters are ideal low-pass:

## Slide 40: Example: Sinc Pulses
Suppose that
  (no impairments)
Then,
  1
Hence, .
Recover symbols exactly. No ISI

## Slide 41: Example: Sinc Pulses with Delay
Suppose that
Channel has gain and delay:
Then,
Similar calculation as before:

## Slide 42: Flat Channels
Suppose that
  in
  “Flat” over the channel.
Then, effective discrete-time channel is
  No ISI
Conclusion: When channel is “flat” over band, equalization is not needed

## Slide 43: Numerically Computing the Channel
For most real channels, we cannot analytically compute
  Transmit and receive filters have complex frequency response
  Channels can many taps at arbitrary delays
But, we need for proper simulation of communication systems
Common solution: Approximately compute numerically
Ideal A/D
Ideal D/A

## Slide 44: Numeric Computation via Discretization
Baseband channel frequency response with filtering:
Effective discrete-time frequency response:
  Assume no aliasing.
Discrete-time impulse response:
Evaluate integral by discretization:
  Take points
  Writing in terms of
  Summation can be computed via an IFFT

## Slide 45: Example: Two Path Channel
Sample rate = MHz
  Sample rate for an 8 channel 5G New Radio system at 120 sub-carrier spacing
(zero-order hold ADCs)
has two paths:
  LOS path: Gain -10 dB, delay = 0
  NLOS path: Gain -15 dB, delay = 10 ns
In a wireless system, this would correspond to a path difference of m

## Slide 46: MATLAB Code

## Slide 47: Outline
Receiver filtering and sampling
Perfect reconstruction with orthonormal modulation
General channels: Time-domain analysis
General channels: Frequency-domain analysis
PSD Analysis
Practical RX filter design
Channel sounding

## Slide 48: PSD of a Sampled Signal
Suppose that
If there is no aliasing:
Now, look at auto-correlation:
Hence, if there is no aliasing
With aliasing:

## Slide 49: PSD of the Receiver
We have
By sampling result, discrete-time PSD is:
Without aliasing:
ADC
RX complex baseband
RX complex symbols

## Slide 50: Units in RX Chain: Time Domain
In time-domain:
Units of = power = energy / time
We take convention: = 1 / (time*sample)
Then: =
Hence:
ADC
RX complex baseband
RX complex symbols

## Slide 51: Units in RX Chain: PSD
Units of = power/Hz = energy
Units of
Units of
Units of per radian
ADC
RX complex baseband
RX complex symbols

## Slide 52: Sample problem (Solution on board)
Received PSD and filter as shown
Two components:
  Desired signal
  Nearby adjacent carrier signal
Assume they are uncorrelated
  Hence powers add.
Draw discrete-time PSD
  Sample rate = 80 Msamples / sec
  Sample rate = 20 Msamples / sec
Desired
Interference
MHz
dBm/Hz
MHz
PSD
[dBm/Hz]
Fillter gain
[dB/samp/Hz]

## Slide 53: Outline
Receiver filtering and sampling
Perfect reconstruction with orthonormal modulation
General channels: Time-domain analysis
General channels: Frequency-domain analysis
PSD Analysis
Practical RX filter design
Channel sounding

## Slide 54: Problems with Analog Filtering
Up to now, we have considered two stage filtering
  Filtering:
  Sampling / ADC:
Problem: Filtering is performed in analog
  Desire sharp filters to remove close adjacent carrier
  Difficult to design sharp filters
Analog filter
ADC
RX complex baseband
RX complex symbols

## Slide 55: Typical Digital Implementation of RX Filtering
Use combination of analog and digital filtering in four steps:
Step 1. Analog filtering
Step 2. Sample at times symbol rate:
  = oversampling ratio
Step 3. Digitally filter:
Step 4. Decimate: .
  Takes one every samples
Digital filter
ADC
RX complex baseband
RX complex symbols,
Symbol rate =
Sample rate=
Analog filter
Decimate by

## Slide 56: Frequency Domain Analysis
Step 1:
Step 2: Sampling at :
Step 3: Digital filtering:
Step 4: Decimate:
Assuming no aliasing: Effective RX pulse shape is

## Slide 57: Frequency Domain Analysis: PSD
Step 1:
Step 2: Sampling at :
Step 3: Digital filtering:
Step 4: Decimate:
Assuming no aliasing: Effective RX pulse shape is

## Slide 58: Sample problem (Solution on board)
Received passband signal as shown
Two components:
  Desired signal
  Nearby adjacent carrier signal
Draw the following:
  Complex baseband after mixing at
  Response after analog filtering with cutoff MHz
  Sampling at 40 Ms/s
  Digital filtering with
  Downsampling by 2
GHz
MHz
GHz
MHz
Desired
Interference

## Slide 59: Filter Design
Effective pulse shape:
Want to be low-pass with cutoff
Typical design for analog filter
  passband up to , Stopband
  Removes images before sampling
  Large transition region. Easy to design
Design spec for digital filter
  Low pass with digital cut-off frequency
  Typically very sharp to remove close adjacent carrier

## Slide 60: Summary of Sampling Relations
Operation | Time domain | Frequency-domain | PSD
Ideal DAC |  |  | 
Digital upsampling |  |  | 
Ideal ADC |  |  | 
Ideal ADC. No aliasing |  |  | 
Digital decimation |  |  | 
Digital decimation. No aliasing |  |  | 
Operation | Time domain | Frequency-domain | PSD
Ideal DAC |  |  | 
Digital upsampling |  |  | 
Ideal ADC |  |  | 
Ideal ADC. No aliasing |  |  | 
Digital decimation |  |  | 
Digital decimation. No aliasing |  |  | 

## Slide 61: Summary of Units
Operation | Quantity | Time domain units | PSD units
TX symbols |  | : Energy per sample | Energy per sample per radian
TX modulation |  | Samples / sec | Samp / Hz = Samp x sec
 |  | Energy / sec = power | : Power / Hz = Energy
RX signal |  | : Energy / sec = power | : Power / Hz = Energy
RX filtered & sampled |  | 1/(samp x time) | 1/(samp x Hz)=time/samp
 |  | Energy per sample | Energy per sample per radian
Operation | Quantity | Time domain units | PSD units
TX symbols |  |  | 
TX modulation |  |  | 
RX signal |  |  | 
RX filtered & sampled |  |  | 

## Slide 62: Outline
Receiver filtering and sampling
Perfect reconstruction with orthonormal modulation
General channels: Time-domain analysis
General channels: Frequency-domain analysis
PSD Analysis
Practical RX filter design
Channel sounding

## Slide 63: Channel Sounder
Measure channel
Useful for:
  Wireless propagation analysis
  Measure multipath components, signal strengths, directions of arrival
  But, also good for debugging any front-end
MmWave and sub-THz channel sounder by Rappaport lab
https://wireless.engineering.nyu.edu/mmwave-5g-and-6g-channel-sounder/
TX
RX
Channel impulse response

## Slide 64: FFT-Based Channel Sounding
Effective discrete-time channel:
Select period
Repeatedly transmit
Receiver will get:
Recover
Get channel response:
Learn from calibration
Estimate
Provides a discrete estimate of the channel.
More in the lab