## Slide 1: Unit 7: Synchronization and Matched Filtering
EL-GY 6013: Digital communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Describe the synchronization mechanisms in common commercial standards
Formulate binary decision tasks as hypothesis testing problems
Compute the LRT detector for a hypothesis testing problem
Compute error probabilities and optimize the threshold
Formulate signal detection as a hypothesis test
Describe and analyze the matched filter detector
Analyze various non-idealities including clock offset, auto-correlation and multi-path
Simulate the MF detector for real systems

## Slide 3: This Unit
Channel coding
Symbol mapping
Coded bits
TX filter DAC
IQ symbols
Analog baseband
Upconversion
Info bits
Passband
Channel
Down-conversion
RX filter and ADC
Sync
Equalization
Symbol demod
Channel decoding
RF
“Noise”

## Slide 4: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection at a Known Delay
Match Filter SNR and Error Probabilities
Match Filtering Convolution with an Unknown Signal Delay
Automatic Gain Control (AGC)
Appendix 1. Error Probability Calculation Details
Appendix 2. Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 5: Synchronization and Detection Problem
Two key problems in most communication receivers:
  Detect if a transmitter is present
  Synchronize to the transmitter
Basic first step in any communication process
Assumes the transmitter broadcasts a signal
Receiver must detect and synchronize to it
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 6: Ex 1: 802.11g Transmission
All data is transmitted in frames
Frames may arrive at any time
Each frame begins with known preamble
  Common to all frames
RX station listens for preamble to detect:
  Presence of frame.
  If frame is present, determines timing delay of the remaining frame
Frame
PLCP header
MAC PDU
Preamble

## Slide 7: 802.11g PLCP Header Details
PLCP header details:
  Preamble: Used for initial detection, synchronization, channel estimation
  Rate: Signals MCS for service bits & MAC PDU
  Length: Number of OFDM symbols in frame
  Service: Scrambler sync
MAC header: Contains MAC layer control info
  Segmentation, MAC addresses, …
MAC FCS: frame check sum (used to detect errors)
Preamble
(16 us)
Rate
(4bits)
Length
(12 bits)
Service
(16 bits)
MAC header
PLCP header
Coded at lowest rate
Rate indicated in PLCP header
Payload
(MAC SDU)
MAC PDU
FCS

## Slide 8: Ex 2: LTE Downlink Primary Sync Signal (PSS)
Each cell transmits periodically PSS
  Narrowband, short (71.4 us x 1.08 MHz)
  One of 3 PSS signals
Once PSS is detected, mobile (UE) knows frame timing
  Decodes subsequent signals SSS, broadcast, …
Frequency

## Slide 9: Ex. 3. 5G New Radio Beam Sweeping
Directional synchronization for mmWave
Transmit multiple SS Burst
  One in each direction
MmWave typically use 120 kHz subcarrier spacing
With 120 kHz SCS:
  SSB = 4 OFDM symbols = 35.7 s
  Each SSB, contains a PSS
  PSS time duration = 1 OFDM symbol = 8.92 s
  Bandwidth = 127 SC = 15.24 MHz
  Up to 64 SS Bursts / burst period
  Typical SSB periodicity = 20 ms

## Slide 10: Simple Synchronization Model
TX sends a preamble / synchronization signal
  Complex baseband samples.
  Sample rate
If signal is present at RX:
  : Complex channel gain
  : Integer delay
Problem detect if signal is present or not.
  If so, what is the delay
For now, we assume:
  Integer delays, no multipath
  Will address these issues later
Delay=
TX
RX

## Slide 11: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection at a Known Delay
Match Filter SNR and Error Probabilities
Match Filtering Convolution with an Unknown Signal Delay
Automatic Gain Control (AGC)
Appendix 1. Error Probability Calculation Details
Appendix 2. Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 12: Hypothesis Testing
Classic problem in statistics or decision theory
Observe data
Two possible hypotheses for data
  H0: Null hypothesis
  H1: Alternate hypothesis
Model statistically:
  Assume some distribution for each hypothesis
  Each density is the likelihood of
Problem: Determine which hypothesis is true given data

## Slide 13: Applications
Many applications
Pattern recognition:
  Does this image contain a face or not?
  Is this person X?
Detection:
  Is the transmitted bit 0 or 1?
This lecture: Is a signal present or not?

## Slide 14: Simple Example
Scalar Gaussian
In this case:
Saw this earlier in BPSK transmissions
Max likelihood detector from earlier
  Selects the most likely hypothesis
  In this case

## Slide 15: Types of Errors
For binary detection problems, there are two errors:
  Type I error (False alarm): Decide H1 when H0
  Type II error (Missed detection): Decide H0 when H1
In many problems, the consequences of these errors is different
Example: Medical diagnosis
  False alarm: You tell the patient he is ill, when he is fine
  Missed detection: You miss the illness
  Consequences are different
Given detector, we define two error probabilities:
  False alarm probability:
  Missed detection probability:

## Slide 16: Likelihood Ratio Test
We can tradeoff the error probabilities with a likelihood ratio test:
Likelihood ratio test (LRT)
  is an adjustable threshold
  Increasing Lowers , but lowers
Often performed in log domain
Note that corresponds to maximum likelihood detector

## Slide 17: Gaussian Example
Scalar Gaussian case:
Log likelihood ratio:
LRT: if and only if
  is an adjustable threshold

## Slide 18: Computing Error Probabilities
From previous slide, LRT detector is:
FA probability:
  This is the area under the curve (blue)
  For Gaussian:
MD probability
  This is the area under the curve (orange)
  For Gaussian:

## Slide 19: Tradeoff
Tradeoff between and
Increasing threshold
  Decreases false alarms
  But increases missed detections
Selection of optimal threshold
  Depends on the application
  What are the relative costs of these errors?

## Slide 20: ROC Curve
Receiver operating characteristic
Plot of vs.
Trace out:
Random guessing achieves:
Higher the line is better

## Slide 21: Neyman-Pearson Theorem
Theorem: Suppose that an LRT obtains . Then any other test with will have a less than or equal to the LRT.
LRT is the most powerful test
Obtains best vs. performance

## Slide 22: In Class Exercise

## Slide 23: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection at a Known Delay
Match Filter SNR and Error Probabilities
Match Filtering Convolution with an Unknown Signal Delay
Automatic Gain Control (AGC)
Appendix 1. Error Probability Calculation Details
Appendix 2. Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 24: Simple Synchronization Model
TX sends a preamble / synchronization signal
  Complex baseband samples.
  Sample rate
If signal is present at RX:
  : Complex channel gain
  : Integer delay
Problem detect if signal is present or not.
  If so, what is the delay
For now, we assume:
  Integer delays, no multipath
  Will address these issues later
Delay=
TX
RX

## Slide 25: Detect as a Hypothesis Test
At each delay , we consider two hypotheses:
Signal is present:
  is a complex, baseband channel gain
  Recall that we are assuming a single path channel (for now)
Signal is absent:
In both cases, assume is white noise:
Delay=

## Slide 26: Detection Problem with a Known Delay
Given :
  RX signal
  Target signal
  Delay hypothesis:
Which “hypothesis” is more likely?
  Signal is present: or
  Signal is absent:
Channel gain is not known
Next section, we will also learn the delay
Delay=

## Slide 27: Hypothesis Test in Vector Form
Without loss of generality, assume:
  Delay
  Target signal length
Define vectors:
Write two hypotheses in vector form:
  [Signal present]
  [Signal absent]

## Slide 28: Projection
Hypotheses in vector form:
  [Signal present]
  [Signal absent]
Projection coefficient of onto is:
  For signal detection is called the (scaled) matched filter
Key idea: Declare signal present when is large
Signal is detected if there is sufficient energy in target signal space

## Slide 29: Match Filter Detector
Given two hypotheses:
  [Signal present]
  [Signal absent]
Match filter energy detector:
  Compute scaled MF detector:
  Measure energy:
  Declare
Value is a threshold

## Slide 30: MF Example
Suppose target signal is
  Target signal norm is:
Suppose that threshold is
Case 1: RX signal is
  Signal is detected!
Case 2: RX signal is
  No signal is detected

## Slide 31: MF Normalization
Up to now, we have used the scaled or normalized MF:
Often, we will use the un-normalized MF:
Detection method is the same, just the threshold changes:

## Slide 32: MF in Continuous-Time
Target signal:
RX signal:
Un-normalized MF is:
Normalized MF is:
Example: for
Then:

## Slide 33: Units
Target signal: is any units, say W
Then: sec
Say RX signal has units W
Then, has units
Hence, normalized MF output squared is:
  has output of energy

## Slide 34: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection at a Known Delay
Match Filter SNR and Error Probabilities
Match Filtering Convolution with an Unknown Signal Delay
Automatic Gain Control (AGC)
Appendix 1. Error Probability Calculation Details
Appendix 2. Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 35: SNR of the MF Detector
Suppose signal is present:
Compute scaled MF detector:
Then:
Signal energy:
Noise energy:
SNR of the MF detector output:

## Slide 36: SNR and RX Power
From previous slide, SNR is
Total RX energy in time window
Noise PSD
Example:
  Suppose RX power is dBm, integration time dBm/Hz
  In linear scale so
  In dB:
  Therefore: dB

## Slide 37: Error Probabilities
Consider normalized MF: where we detect signal if
It can be shown (see Appendix 1)
Probability of false alarm:
  Decreases with threshold
Probability of missed detection:
  Complicated expression of SNR and threshold (see Appendix 1)
  Decreases with and increases with threshold

## Slide 38: Selecting the Threshold
From previous slide:
Set threshold to
  target FA probability = Maximum allowable FA rate
Then, will depend on the SNR
Typical FA probabilities are very low: to
As a result, SNR for detection is often high:
  Can be to 20 dB

## Slide 39: Simulation
Theoretically calculated threshold based on PFA target
Simulate PMD based on SNR

## Slide 40: Problems with MF
Consider normalized MF:
Problem 1: FA threshold requires knowledge of
  Threshold
Problem 2: Any signal with can make large
  Any high-power signal can trigger a detection
Example
Target
RX matches target for some
But is low
RX does not match target well
for any
But is high

## Slide 41: Correlation Coefficient Method
Correlation coefficient method:
  Compute
  Signal is detected if for some
Property 1:
  = Represents fraction of energy of in span of
  Signals do not trigger detection just by being large
Property 2:
  FA alarm target does not depend on
  Suppose
  Distribution does not depend on scaling
  Can show (HW)

## Slide 42: SNR Estimate
Given vectors and , can show that the best linear estimate of
Hence, SNR estimate is:
Thus, correlation coefficient provides an estimate of the SNR:

## Slide 43: In Class Exercise

## Slide 44: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection at a Known Delay
Match Filter SNR and Error Probabilities
Match Filtering Convolution with an Unknown Signal Delay
Automatic Gain Control (AGC)
Appendix 1. Error Probability Calculation Details
Appendix 2. Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 45: Match Filtering with Unknown Delay
Synchronization signal
RX signal at delay :
Problem: Detect if signal is present. If so, what is the delay ?
Match filter (without normalization) at delay is:
Hypothesis test:
  Detect signal at delay at

## Slide 46: Match Filtering as a Convolution
Match filter (without normalization) at delay is:
Define adjoint signal:
  Complex conjugate and time reversal
MF output can be computed via a convolution:
Filter with
Peak detection
Detected signal locations

## Slide 47: Boundary Conditions
Match filter (without normalization) is:
Suppose:
  Target has samples
  RX signal has samples
Then, we can test up to hypotheses:
Compute in MATLAB with “valid” mode
  If and are column vectors
Max delay
Min delay

## Slide 48: Correlation Coefficient Method
To compute correlation coefficient:
  Compute un-normalized MF:
  Moving average RX energy:
  Signal energy:
Then, correlation coefficient squared is:
Can be perform with two parallel convolutions

## Slide 49: Further Analysis Details
We need to examine three key practical issues that degrade performance
Preamble auto-correlation
Multi-path
Carrier offset

## Slide 50: Signal Auto-Correlation
Consider what happens with no noise:
  , “True” delay
Run match filter:
Can show output is:
  autocorrelation of transmitted signal
Since we want small for we want: for
Many sequences with low auto-correlation
  Golay, Walsh, ….
Auto-correlation of Golay 128 sequence
Used in 802.11ad preamle

## Slide 51: Multipath
Up to now we have assumed that there is a single path:
But, in reality there is often multipath:
  Due to multi-path in channel and pulse shape filtering
Match filter has delayed copies of auto-correlation:
  One peak in MF output for each path
Ex: Two path channel
Path at
Path at

## Slide 52: Frequency Offsets
When initially searching for a preamble, there may be a significant carrier offset
Causes a phase rotation in samples:
  is the phase rotation per sample
  , frequency error, sampling rate
Must integrate over range where phase does not change significantly
  Pre-amble length must be
Example: Suppose the carrier offset =10 ppm, GHz and Gs/s
  samples
  In time duration, this is us
  A very short time before the signal is completely rotated

## Slide 53: Detailed Simulation Example
Transmit 128 length Golay pre-amble
Filter through channel with single (possibly fractional) delay
Set threshold for FA target of per 1000 samples
Measure MD probability as a function of the SNR
Filter with
Peak detection
Detected signal locations

## Slide 54: Calibration
Need to calibrate the FA probability and delay offset
Threshold
PFA
True Delay
Estimated Delay

## Slide 55: Missed Detection
Loss of about 3dB with fractional delay offset
Signal energy is split in two samples
Need to use over-sampling to compensate
  See lab

## Slide 56: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection at a Known Delay
Match Filter SNR and Error Probabilities
Match Filtering Convolution with an Unknown Signal Delay
Automatic Gain Control (AGC)
Appendix 1. Error Probability Calculation Details
Appendix 2. Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 57: Automatic Gain Control
AGC goal: Bring RX signal to “correct” level
Tradeoff of two factors
Want high gain: Overcome noise after AMP
But gain too high saturates RX
AGC finds optimal level
Variable gain AMP
Gain
control
RF front end
Digital baseband

## Slide 58: Mathematical Model
RF front-end
  Linear gain with noise:
  Noise after AMP
  Memoryless nonlinearity:
  and have PSD and
Digital baseband
  Measures RX power or SNR
  Controls gain
Variable gain AMP
Gain
control
RF front end
Digital baseband
+
+

## Slide 59: Analysis with No Nonlinearity
With no nonlinearity:
PSD of signal component in output:
PSD of noise in output:
Output SNR:
Variable gain AMP
+
+

## Slide 60: Analysis with No Nonlinearity Example
Output SNR from previous slide:
Fig to left: dB, dB
Observations with no nonlinearity:
  Increasing gain always improve output SNR
  Saturates at as
Design principle:
  Have high SNR (low noise) in first stage
  Increase gain to overcome noise in later stage
Typical RF design starts with a low noise amplifier (LNA)
Variable gain AMP
+
+

## Slide 61: Example with Saturation Nonlinearity
With high gain :
  Signal becomes large
  May saturate component distortion
Saturation occurs in many RF components
  E.g., mixer, LNA
Example:
  30 dB, 10 dB
  Nonlinearity is a saturation: Clips at
  Saturation level 50 dB
We see ideal gain trades off gain and NL distortion
+
+
Gain too high NL distortion
Gain too low Signal too small relative to
No NL
Ideal gain
With NL

## Slide 62: Example with ADC
Example ADC:
  Similar to quantization + saturation
  Saturates at with bits
With finite bit width
  Set gain to not overflow ADC
+
Gain too high NL distortion
Gain too low Signal too small relative to
Ideal gain
ADC

## Slide 63: Practical Gain Control
Measure RX power
  RX power over last symbols
Adjust gain:
  Decrease gain
  Increase gain
Threshold
  Set to ensure signal is not saturating
Variable gain AMP
Gain
control
RF front end
Digital baseband
+
+

## Slide 64: Gain Control in 802.11
WLAN systems require very fast AGCs
STF (short training field). Duration is s
  Used for detection and AGC
  Typically set AGC in first ~2
  Perform detection in remaining
Cannot detect STF until AGC has run
  Otherwise, signal will be too low in SNR or too distorted
AGC is implemented in hardware

## Slide 65: The 9361 Integrated Circuit
Gain performed in at least three stages
  LNA gain control at RF
  TIA (transimpedance AMP) gain at IF
  Digital gain during digital filtering
Single gain setting selects all three gains
  Ensure all intermediate points do not overflow
RX
TX

## Slide 66: AGC in the Pluto
MATLAB interface gain control
AGC Fast Attack
  AGC automatically performed in HW
  Ideal for WLAN with fast gain
  But host has no visibility to gain selected
Manual
  User can manually select gain
  We will use this in lab
  But it is very slow
  Just for education

## Slide 67: SDR Lab
https://github.com/sdrangan/sdrlab/tree/main/lab05_gain

## Slide 68: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection at a Known Delay
Match Filter SNR and Error Probabilities
Match Filtering Convolution with an Unknown Signal Delay
Automatic Gain Control (AGC)
Appendix 1. Error Probability Calculation Details
Appendix 2. Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 69: False Alarm
False alarm
  Under
  Statistic
  This is a linear function of a Gaussian
  Hence,
  Hence is exponential with

## Slide 70: Missed Detection
Under
Statistic
Similar to FA calculation:
Can show:
  is a non-central chi squared with degrees of freedom
  Non-centrality parameter

## Slide 71: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection at a Known Delay
Match Filter SNR and Error Probabilities
Match Filtering Convolution with an Unknown Signal Delay
Automatic Gain Control (AGC)
Appendix 1. Error Probability Calculation Details
Appendix 2. Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 72: Likelihood Ratio Test
In vector form:
  [Signal present]
  [Signal absent]
Likelihoods:
  ,
  Cannot apply regular LRT since parameters are unknown
  GLRT

## Slide 73: Generalized Likelihood Ratio Test
Null hypothesis
Present hypothesis:
  Minimize over :
GLRT:
Details in class