## Slide 1: Unit 4: Signal Space Theory
EL-GY 6013: Digital communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Determine if a set is a vector space or not
Find the dimension for a vector space or subspace. Find a basis
Find a signal space for a set of signals.
  Compute the degrees of freedom and rate for signal set in a signal space
  Find the representation of a signal in signal space for a given basis
Find the number of DoF per second of a band-limited signal
Determine if vector or signals are orthogonal
Find an orthonormal basis.
Compute representations of signals in an orthonormal basis
Find the energy per DoF in an orthonormal basis

## Slide 3: Outline
Motivation for the signal space model
Vector spaces, bases and dimension
Signal spaces, rate and degrees of freedom
Nyquist Theorem and degrees of freedom in band-limited signals
Inner products and orthogonality
Orthonormal bases and energy per degree of freedom

## Slide 4: Algorithmic Model of a Typical Transmitter
Up to now, we have considered a standard transmitter with three steps
  Symbol mapping
  TX filtering
  Upconversion
Symbol mapping
Input bits
TX filter DAC
IQ symbols
Analog baseband
Output signals
(baseband or RF)

## Slide 5: Abstract Signal Space Model of a Transmitter
Maps bits to signals
Signals belong to a vector space
Symbol mapping
Input bits
TX filter DAC
IQ symbols
Analog baseband
Output signals
(baseband or RF)
Input bits
Output signals
(in a vector space)
=

## Slide 6: Why Use the Signal Space Model?
Analysis is not limited to a specific TX architecture
  Applies to any communication system
Describes fundamental parameters of the system
  Rate and degrees of freedom
  In next unit, we will also introduce a third parameter which is SNR
Some calculations are easier in the transformed space
Provides a geometric model to understand communication
Input bits
Output signals
(in a vector space)

## Slide 7: Outline
Motivation for the signal space model
Vector spaces, bases and dimension
Signal spaces, rate and degrees of freedom
Nyquist Theorem and degrees of freedom in band-limited signals
Inner products and orthogonality
Orthonormal bases and energy per degree of freedom

## Slide 8: Vector Spaces
Definition: A vector space over a field or : A set V with operations:
  Addition:
  Scalar multiplication:
We will use as a placeholder for the field
Commutative, associative, distributive relationships hold
Vector subspace: Subset that is also a vector space.

## Slide 9: Vector Space
Set of n-dim vectors ]
  Each element
  Can be row or column vectors
  Or just vectors
Standard addition and scalar multiplication rules
Make sure you know how to do these operations

## Slide 10: Example Problem
Which of the following are vector subspaces of
set of s.t
set of s.t
set of s.t
set of s.t
set of s.t
Solutions on board

## Slide 11: Vector Spaces of Functions
In communications, we often need to consider vector spaces of functions
Example:
  Set of continuous functions on
  Each “vector” is a function
  Can be complex or real-valued
We can add and subtract functions as usual:
Ex:
  If then

## Slide 12: Example Problem
Which of the following are vector subspaces
Set of differentiable functions
Set of functions
Set of polynomial functions
Fix . Let = set of functions with
Solutions on board

## Slide 13: Linear Span
Let some vector space and
A linear combination of is a vector of the form:
Span: The set of all linear combinations of the vectors:
  This is a vector subspace of
  are said to span if
Example: In is the plane that contains the two vectors

## Slide 14: Linear Independence
Vectors are linearly independent if:
  Any non-zero combination of the vectors is non-zero.
  If vectors are not linearly independent, then they are linearly dependent
Example: Consider case of two vectors
  are linearly dependent if and only if or
  That is, vectors are in the same direction

## Slide 15: Basis and Dimension
Given vector space
Vectors are a basis for if
  are linearly independent and span
This means that every can be uniquely written as:
Say are the coordinates of in the basis
Dimension of

## Slide 16: Simple Vector Example
Vectors [1,2], [3,6] are linearly dependent since:
Vectors are linearly independent:
  Why? Suppose that
  Then:
  Matrix is invertible. So this system of equations has a unique soln:
  Hence are a basis.
Write as a linear combination of
Performing these calculations for larger dimension matrices by hand is generally difficult

## Slide 17: Standard Basis and Change of Basis
Standard basis of :
  A “1” in position
Any vector
  Hence are the coordinates in the standard basis
Change of basis:
  Suppose is another basis
  Want to find coordinates

## Slide 18: Example
Suppose
in the standard basis
Find coefficients of in basis
Solution:
  Solve
  Get
Standard basis
New basis

## Slide 19: Function Example
Consider set of continuous functions
Let for some
Then are linearly independent.
  Why? Suppose that
  Then: for all (sometimes we say is identically zero)
  But is a polynomial of degree
  A polynomial for all if and only all the coefficients are zero (Follows from the fact that any non-zero polynomial of degree has at most real roots)
Since we can make arbitrarily large, has infinite dimension
  There are an arbitrary number of linearly independent vectors

## Slide 20: Outline
Motivation for the signal space model
Vector spaces, bases and dimension
Signal spaces, rate and degrees of freedom
Nyquist Theorem and degrees of freedom in band-limited signals
Inner products and orthogonality
Orthonormal bases and energy per degree of freedom

## Slide 21: Abstract Transmitter and the Signal Set
Abstract transmitter:
  Input is a set of bits
  Outputs one of a finite set of signals
  For now, we will consider only a finite set of bits
In general, there are possible output signals
Definition: We call the signal set
  We say is the number of bits in
This model is not specific to any architecture
Input bits
Output signals

## Slide 22: Example
Suppose we linearly map QPSK symbols:
There are input bits
There are output signals
Each set of bits
  Each bit pair gets mapped to a symbol
  We obtain symbols
  Results in signal after linear modulation

## Slide 23: Signal Space
Consider a signal set
  Can be either a set of received signals or transmitted signals
  Can be in discrete-time, analog baseband or analog RF
  For now, we consider only finite signal set,
  But signals can be infinite in duration or finite
A signal space for is any vector space that contains
Note: is not itself a vector space
  It is a discrete set
  But it is contained in a vector space.

## Slide 24: Signal Space Bases
Let be a signal set
Suppose signal space containing
Since is a vector space it has a basis:
Then, each signal can be expanded as:
The vector is the coordinate vector of in the basis
  The components are the coordinates

## Slide 25: Degrees of Freedom and Rate
Let be a signal set
Signal space theory has two key parameters
Degrees of freedom:
  The smallest dimension of a signal space with
  If =#degrees of freedom, then there are basis vectors with
Rate: The rate of a signal set in a signal space with dimension is:
  Represents the amount of information transmitted per DoF

## Slide 26: Complex vs. Real DoF
Often signals or are complex-valued
Typically use a complex vector space
  Coordinates will be complex
  We say there are complex degrees of freedom
Or we can convert to a vector space over
  Define basis with vectors: and
  Then, we can write:
  So, there are real degrees of freedom

## Slide 27: Example
Consider the four functions shown to the right
Find degrees of freedom of
Find a signal space for with dimension
Find a basis for
Find the coordinate vector of each in the basis
Time
1
0
2
Time
1
0
3
Time
1
0
1
Slope=1
Slope=-2
-2

## Slide 28: Example Solution
1
0
3
1
0
1
Slope=1
Slope=-2
Can use basis vectors
So, there are degrees of freedom
bits
Rate bit / DoF
1
0
1
1
0
Slope=1
1
0
2
-2

## Slide 29: Visualizing the Coordinate Vectors
1
0
3
1
0
1
Slope=1
Slope=-2
1
0
2
-2

## Slide 30: Signal Space View of Transmitter
Signal space view
  Input is a set of bits
  Outputs one of a finite set of signals
  Each output has a coordinate vector
So, abstractly transmitter maps:
Input bits
Coordinates in a signal space

## Slide 31: Signal Space for Pulse Shaping
Suppose that we transmit symbols via linear modulation:
Take basis:
Then:
So, are contained in a signal space with (complex) degrees of freedom
Coordinate of in basis are they symbols

## Slide 32: Example for 16-QAM
Transmit:
Suppose each symbol is 16-QAM.
  bits per symbol
Number of bits per signal:
Rate is bits per DoF

## Slide 33: Unique Decodability
Suppose that we use linear modulation with functions
Definition: We say modulation is uniquely decodable if, for any , we can uniquely determine
Uniquely decodable is the minimum we can expect of a modulation scheme:
  If modulation is not uniquely decodable, there are at least two different that give rise to
  Hence, a receiver will not know which was transmitted
  So, there is no hope of estimating the correct symbols reliabily without further information
  …And we haven’t even considered any impairments like noise

## Slide 34: Unique Decodability and Degrees of Freedom
Theorem: Consider linear modulation
  Then, modulation is uniquely decodable if and only if are linearly independent
Proof: This is an immediate consequence of linear independence
Implication:
  Suppose we use linear modulation in a signal space where
  Suppose that has degrees of freedom
  Then, we can transmit at most symbols uniquely
Caveats:
  Even though DoF limits number of symbols, it does not limit number of bits
  We can transmit multiple bits per symbol.

## Slide 35: Outline
Motivation for the signal space model
Vector spaces, bases and dimension
Signal spaces, rate and degrees of freedom
Nyquist Theorem and degrees of freedom in band-limited signals
Inner products and orthogonality
Orthonormal bases and energy per degree of freedom

## Slide 36: Reconstructing a Signal from Samples
Let be a continuous-time signal
Suppose we are given samples
Reconstruction problem:
  Estimate from sample
A classic problem in signal processing
Ideal A/D
Sampling
Reconstruction

## Slide 37: Nyquist Theorem
Suppose is band-limited: for
  is the single-sided bandwidth
We are given samples
Nyquist theorem: If then, we can reconstruct by:

## Slide 38: Nyquist Theorem Proof
A simple picture proof in frequency-domain
FT of original bandlimited
DTFT of sampled signal
gets mapped to
3
FT of upsampled signal

## Slide 39: Nyquist Theorem Proof
Sinc filter
From previous slide
FT of upsampled signal
FT of filtered upsampled signal:

## Slide 40: Sinc Interpolation Visualized
Sinc interpolation:
Around each sample
  Take a sinc function
  Shift to center at
  Scale by

## Slide 41: DoF for Bandlimited Signals
The following is an important consequence of Nyquist Theorem
Theorem (Loose non-rigorous statement): Suppose that is a signal space such that:
  is band-limited to for all
  for (i.e. time-limited to seconds)
  Then has at most degrees of freedom
Thus, DoFBandwidth Time
We say there are DoF per second
This is non-rigorous statement
  Rigorous statement would properly bound for

## Slide 42: “Proof” of DoF Statement
If then
  is band-limited to and
  for (i.e. time-limited to seconds)
Since it is band-limited,
Since it is time-limited, for
Thus,
This summation has only terms
So all signal can be expressed as span of terms

## Slide 43: Example
Suppose you download data
  Download time is 10 seconds
  Bandwidth is MHz (a standard bandwidth for the largest single LTE channel)
  Rate is 1.5 bits / DoF available
How much do you download?
Solution:
  There are DoF
  You can download Mbits
  This is 43.75 MB of data

## Slide 44: Outline
Motivation for the signal space model
Vector spaces, bases and dimension
Signal spaces, rate and degrees of freedom
Nyquist Theorem and degrees of freedom in band-limited signals
Inner products and orthogonality
Orthonormal bases and energy per degree of freedom

## Slide 45: Inner Product in
Inner product in :
  = complex conjugate of
  Note: Some texts use
If and are column vectors, then
Examples:
  and
  and

## Slide 46: Inner Product on a General Vector Space
Suppose is a vector space over
Definition: An inner product on is a function such that:
  Conjugate symmetry:
  Linearity in the second argument:
  Positive definiteness: and
A vector space with an inner product is called an inner product space
Regular inner product in satisfies the above properties
Derived property: Conjugate linearity in the first argument:

## Slide 47: Inner Product Geometry
Any inner product induces a norm:
  Note so the square root can be taken
  Easy to verify that it is satisfies the required norm properties
For , this is the standard 2-norm:
Triangle inequality:
Cauchy-Schwartz inequality:
Write:
  angle between vectors
  Represents “similarity” between vectors
  For real vetors,

## Slide 48: Inner Products on Functions
Let be two functions on
  Possibly complex-valued
Define inner product:
  Same as inner product in with sum replaced by integral
Norm squared is the energy:
  Signal energy
Parseval’s theorem
The space = set of with finite energy

## Slide 49: Example Problem
Let
  Assume
Find
Find
Solution:

## Slide 50: Orthogonality
Orthogonal vectors:
  Pythagoras Theorem: +
  Write .
For
  are right angles to one another
If , the signals are orthogonal if:
A set of vectors is orthonormal if:
  Pairwise orthogonal: when
  Unit energy:
  Could be a finite or infinite set

## Slide 51: Examples of Orthogonal Vectors and Signals
In
In : Any two signals that have non-overlapping support
Complex exponentials: for
Sinc functions:
  We showed these are orthogonal last unit

## Slide 52: Outline
Motivation for the signal space model
Vector spaces, bases and dimension
Signal spaces, rate and degrees of freedom
Nyquist Theorem and degrees of freedom in band-limited signals
Inner products and orthogonality
Orthonormal bases and energy per degree of freedom

## Slide 53: Orthonormal Basis
Let be any vector space
Definition: A set is orthonormal if:
  for all (all vectors have unit energy)
  for all (different vectors are orthogonal)
Orthonormal linearly independent.
  Why? Suppose that
  Multiplying by we get for all (since )
Consequence: if are orthonormal, then they are a basis for
  Called an orthonormal basis

## Slide 54: Example
Show the vectors are orthonormal:
Solution:

## Slide 55: Unitary Matrices
A matrix is unitary if
  called orthogonal if it is real-valued (i.e. and )
is unitary/orthogonal if and only if one of the following equivalent properties are true:
  The rows of are an orthonormal set
  The columns of are an orthonormal set
  for all
  for all

## Slide 56: Proof of the Unitary Matrix Properties
unitary : Follows from the definition
unitary columns of are orthonormal
  Write where is the -th column
  Then:
  Since
  Hence: for and for all
unitary row of are orthonormal. Same proof as previous but use
unitary

## Slide 57: Coefficients in an Orthonormal Basis
Let be an orthonormal basis
Theorem: Given any , where
Consequence: Find coefficients of in an orthonormal basis is easy
  Just take inner products .
  NO matrix inverse
Proof of theorem
  Since is orthonormal, is unitary
  Since we can write
  But then

## Slide 58: Orthogonal Matrix Transformations
Coefficient in standard basis
Coefficients in orthonormal basis

## Slide 59: Example
Consider the orthonormal set from before:
Let . Find the coefficient expansion in the orthonormal bases
Solution:
  Then

## Slide 60: Finding an orthonormal basis: Gram Schmidt
Let be linearly independent
There exists an orthonormal set such that
Conclusion: Every subspace has an orthonormal basis
Gram-Schmidt Procedure for finding

## Slide 61: Gram Schmidt Example

## Slide 62: QR Factorization
Gram-Schmidt is mostly done on a computer
Use the QR factorization.
Given matrix
  Columns are the vectors that we want to apply the GS procedure to
QR factorization:
  orthonormal set from the GS procedure
  lower triangular matrix has coefficients of vectors in terms of :
LU is another factorization

## Slide 63: Orthonormal Basis of Functions
Up to now, we have defined orthonormal bases for finite-dimensional spaces
Let be a set of functions in
  Could be indexed from also
  could be a bounded or infinite interval
Definition: We say is an orthonormal basis if:
  is an orthonormal set
  For any
This means the approximation is asymptotically exact

## Slide 64: Common Orthonormal Sets and Bases
Set of complex exponentials
  This is a basis of
Set of sinc’s:
  This is a basis of the set of signals band-limited to
Set of rectangles:
  This is an orthonormal set but not a basis

## Slide 65: Energy and an Orthonormal Basis
Suppose is a signal space with DoFs
We can find an orthonormal basis
Given any , we can write
Signal energy is
Parseval’s Theorem:
Proof: On board
In an orthonormal basis, we can compute energy in the coefficients
  Call the energy in the th degree of freedom

## Slide 66: Example Problem
Suppose that has a coefficient representation in an o.n. basis
Suppose coefficients are
What is if the signal energy is -150 dBmJ?
Solution:
  Signal energy is mJ
  By Parseval’s theorem
  Hence mJ / DoF