## Slide 1: Unit 10: Convolutional Codes
EL-GY 6013: Digital communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Encode data using a convolutional code for given a generator polynomial
Compute the rate of the code including tail bits
Represent the code via a trellis diagram and finite state machine
Compute the branch metrics of a code for a memoryless channel
Decode the code via the Viterbi algorithm

## Slide 3: Graduate vs. Undergraduate
Unit 9 on basic codes is skipped for the graduate students
However, a few of the Unit 9 slides are included here for completeness
Grad students who would like a review are encouraged to look at Unit 9

## Slide 4: This Unit
Channel coding
Symbol mapping
Coded bits
TX filter DAC
IQ symbols
Analog baseband
Upconversion
Info bits
Passband
Channel
Down-conversion
RX filter and ADC
Sync
Equalization
Symbol demod
Channel decoding
RF
“Noise”

## Slide 5: Outline
Convolutional codes: encoding and representations
Tree, trellis and state diagrams
Decoding with branch metrics
Viterbi decoding

## Slide 6: Convolutional Codes History
Generates a stream of coded bits from uncoded bits
  Block codes form by terminating the stream
Output stream created by binary FIR filters
Developed originally by Elias (1955)
  Key challenge was decoders. Much study in 1960s.
  Practical, optimal decoders developed by Viterbi,1967.
Can perform within 2-3 dB of Shannon limit.
Instrumental in Pioneer Space program (along with RS codes)
Most widely-used code in industry today: WiFi, cellular
  In the mid 1990s, longer block length cellular codes were replaced with Turbo codes,
  But, these use convolutional codes as basis

## Slide 7: Convolutional Codes
Encode data through parallel binary (usu. FIR) filters
Example convolutional code:
  Rate = ½ (two output bits () for each input bit b[t].
  Constraint length K=3 (size of shift register)
b[t]
c1[t]
c2[t]
z-1
z-1
z-1

## Slide 8: Convolutional Codes Block Implementation
To implement as block code:
  Start with L input bits b[0],b[1],…,b[L-1]
  Append K-1 zero b[L]=b[L+1]=…=b[L+K-2]=0 (called tail bits)
  Generate output bits from each branch
    cj[0], cj[1], … , cj[L+K-2], j=1,…,N where N = number of branches
  Final codeword is concatenation of branch output
    c=(c1[0], c1[1], … , c1[L+K-2],…, cN[0], cN[1], … , cN[L+K-2])
Effective rate: for large
b[t]
c1[t]
c2[t]
z-1
z-1
z-1

## Slide 9: Convolutional Codes Encoding Example
Encode message b = [1 0 1]
Branch outputs c1=[11011] c2=[11001]
Final output c=[11,10,00,10,11] (interleaved)
Rate = 3/10
b[t]
c1[t]
c2[t]
z-1
z-1
z-1
t | b[t] | c1[t] | c2[t]
0 | 1 | 1 | 1
1 | 0 | 1 | 0
2 | 1 | 0 | 0
3 | 0 | 1 | 0
4 | 0 | 1 | 1
Tail bits

## Slide 10: Generator Polynomials: Binary Form
Code polynomials: Binary vector of filter coefficients
Rate 1/3, K=3 example:

## Slide 11: Generator Polynomials: Octal Form
For large constraint lengths (large K), binary form is inefficient
  Engineers often use octal form
  Base 8, each digit 0…7
  Each digit represents three bits
Example:
Binary
Octal

## Slide 12: Multiple Inputs
Examples up to now are R=1/n
Can extend to rate R=k/n
  Add k bits at a time

## Slide 13: In-Class Exercise

## Slide 14: Outline
Convolutional codes: encoding and representations
Tree, trellis and state diagrams
Decoding with branch metrics
Viterbi decoding

## Slide 15: Convolutional Codes as State Machines
Convolutional codes have memory
  Stored in contents of shift registers
  Each input bit changes memory contents
  Output bits are a function of memory and input
Three common ways to represent evolution of the memory:
  Tree diagram
  Trellis diagram
  State diagram

## Slide 16: Encoder States
State of the encoder determined by contents of shift register:
Only need to look at most recent K-1 bits not including the current bit
  Last bit will be shifted out
  There are states
State label |  | 
a | 0 | 0
b | 0 | 1
c | 1 | 0
d | 1 | 1
State label |  | 
a | 0 | 0
b | 0 | 1
c | 1 | 0
d | 1 | 1
b[t-1] b[t-2]

## Slide 17: Tree Diagram
Two branches for each input bit 0 or 1.
Branches labeled by output bits (n bits)
Difficult to use since branches infinitely grow

## Slide 18: Trellis Diagram
Show trajectory through the states
Solid lines: paths with b[t]=0, Dash lines: b[t]=1
Labels are the outputs along each path

## Slide 19: State Diagram
One node per state
Solid lines:
  Transitions with b[t]=0
Dashed lines:
  Transitions with b[t]=1
Labels indicate outputs on each state

## Slide 20: State Machine Functional Description
Finite state machine:
  : Sequence of states,
  : Input sequence
  : Output sequence
Iterative generating sequence:
Initial condition:
State function
Output function

## Slide 21: In-Class Exercise

## Slide 22: Outline
Convolutional codes: encoding and representations
Tree, trellis and state diagrams
Decoding with branch metrics
Viterbi decoding

## Slide 23: ML Estimation
Assume the following dimensions:
  outputs per time steps:
  time steps (including tail bits!)
Channel model:
  For each bit , we make some observation
  Output is probabilistic
  Assume all outputs are independent:
Find ML estimate:
  Maximum over all sequences

## Slide 24: LLR Review
Before studying convolutional codes, consider simple code:
  Codeword has output bits:
  Receive symbols . Each may be binary, discrete, real-valued or complex-valued
  Assume a memoryless channel:
Define LLR:
Theorem: The ML codeword maximizes the LLR sum value function (se Unit 9)

## Slide 25: Example 1: Binary Symmetric Channel
Binary symmetric channel: Output or 1
Error probability
Branch metric:
Observe
Hence maximizing value function:

## Slide 26: Example 2: QPSK Channel
Binary modulation (on a real or imaginary dimension):
Gaussian distribution:
LLR is:
LLR sum value function:

## Slide 27: Branch Metric
Log-likelihood ratio:
  Depends on received symbol
Each branch has an output set of bits
Define the branch metric:
  is the coded outputs on the branch
Describes likelihood that sequence passed through the branch
  Branches with higher branch metrics are more likely

## Slide 28: Branch Metric Maximization
Each branch in trellis has a branch metric
We can write LLR sum value function as:
Interpretation:
  Each code sequence is a path in the trellis
  Value function is the sum of branch metrics on the path
Conclusion: ML estimate is the codeword with the highest total path

## Slide 29: Example
Consider toy Trellis (not a real conv code)
Input:
Output:
  Shown on branches
RX symbols:
  Values shown above Trellis
Assume QPSK channel value function:
  Constant is ignored
:

## Slide 30: Step 1: Compute Branch Metrics
For QPSK channel, branch metric is
On each branch we have labeled:
  (Output Bits, branch)
:

## Slide 31: Step 2: Find the Maximizing Path
For this simple Trellis, we can do this manually
Path is shown with red nodes
Solution:
  Coded sequence: (11), (10), (00)
  Bits: (1,1,0)
:

## Slide 32: Outline
Convolutional codes: encoding and representations
Tree, trellis and state diagrams
Decoding with branch metrics
Viterbi decoding

## Slide 33: Viterbi Algorithm by Example
Iterative solution for finding maximum path in a graph
Key idea: Find the max path one time step at a time
We will illustrate by example: Shown are the branch metrics

## Slide 34: Ex: Time 1
Find total value to get to each node at time 1
  We call these the partial value functions up to time 1
Remember best path to get to node (indicated with green line)

## Slide 35: Ex: Time 2
Add value from Time 1 + branch
Example:

## Slide 36: Ex: Time 3
Add value from Time 2 + branch
Take route with maximum value (shown in green)
Example:

## Slide 37: Ex: Time 4
Add value from Time 3 + branch
Take route with maximum value (shown in green)
Example:

## Slide 38: Ex: Time 5
Add value from Time 4 + branch
Take route with maximum value (shown in green)
Example:

## Slide 39: Ex: Trace back path
Trace back maximum path. Shown in red

## Slide 40: Ex: Read off bits
Read off the bits from the maximum path
ML input bits =

## Slide 41: Complexity
Update of each node requires maxima over branches
There are states, so complexity / time is
Total complexity is
Storage is also . (From the paths)
Summary:
  Viterbi algorithm is linear in block length.
  Can have very long block lengths (often T in the 1000s)
  But, complexity is exponential in constraint length
  Practical decoders limited to or .

## Slide 42: Terminating the Trellis
Recall tail bits are zero: .
Limits the paths at the end of the trellis
Viterbi algorithm should only be done on the zero path.
Very important to not forget the bits at the end.
Otherwise, final bits are not protected.
During tail bits only paths with zero bit inputs.

## Slide 43: Pruning the Path Memory
In current algorithm, path grows to full block length.
Adds storage: Storage is O . Linear in T
Adds delay. No bits can be determined until code is fully decoded.
Many practical implementations:
  Store some finite length of each surviving path.
  Can make decision on bit input after r.
  Rule of thumb: Good performance if .

## Slide 44: Rate Matching Convolutional Codes
Convolutional codes have limited rates, usu. ½ or 1/3.
Obtain other rates through
  Puncturing: Remove coded bits to increase rate
  Repetition: Repeat coded bits to decrease rate
Puncture / repeat pattern is important (see Proakis)
  Try to spread out modified bits
For punctured bits, set corresponding LLRs to zero
  Viterbi decoder just ignores those bits
For repeated bits, add the corresponding LLRs
  Viterbi decoder will increase confidence on that branch

## Slide 45: High Order Constellations
Higher order constellations (eg. 16- or 64-QAM)
Each constellation is a point is a function of multiple bits.
Likelihood does not factorize
  Each symbol r(t) depends on multiple bits
Example 4-PAM (or one dimension of 16-QAM):
  Each symbol likelihood depends on two bits:
Two bits:

## Slide 46: High Order Constellations
To create LLRs for individual bits use total probability rule:
Resulting bitwise LLR:
Two bits:

## Slide 47: High Order Constellations
LLRs can have irregular shapes
Not simple linear function as in BPSK / QPSK case
Often use approximations
More info: Caire, Taricco and Biglieri, “Bit-Interleaved Coded Modulation," 1998.
Two bits:
LLR for c2 LLR for c1

## Slide 48: Convolutional Codes in WiFi
802.11 uses R=1/2 K=7 code.
Length adjusted to packet size
Higher rates (R=2/3 and ¾) achieved through puncturing
Enables decoding as data arrives for ACK fast turnaround
Data symbols
Viterbi decoding
Channel est / sync
Preamble
Check CRC & form ACK
ACK
Turnaround time (<= SIFS = 10us)

## Slide 49: Convolutional Codes in LTE
Convolutional codes in LTE used for:
  Control channels (payload typ 20-40 bits +CRC), and
  Short (< 128 bit) data frames
Larger payloads encoded with turbo codes (discussed later)
Uses rate=1/3 base convolutional code with K=7.
Higher rates achieved via puncturing
Control channels use a sophisticated technique called tail biting to reduce loss on the tail bits

## Slide 50: Decoding Performance
Hard decision loses approximately 1.5 to 2 dB
Constraint length K=7 is sufficient for very sharp error performance

## Slide 51: Different Constraint Lengths
Approximate 1 dB improvement between K=3, 5 and 7
Higher constraint lengths become computationally intractable
Recall decoding complexity is exponential in K

## Slide 52: LLR Quantization
Minimal gains after 16 bit quantization of branch metrics
Recall HD is equivalent to 1 bit quantization
Most commercial implementations use 6-bit LLRs

## Slide 53: MATLAB Convolution Tools
MATLAB comm toolbox
  General convolution encoders & decoders
  Efficient implementation
  Excellent for testing
See demo

## Slide 54: In-Class Exercise