## Slide 1: Unit 11: Information Theory and Capacity
EL-GY 6013: Digital communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Define and compute the Shannon capacity for simple memoryless channels
Identify power-limited and bandwidth-limited regimes of operation
Describe difficulties in achieving the Shannon capacity for practical systems
Mathematically describe the performance of a system relative to the Shannon limit
Define and compute the constellation-constrained capacity

## Slide 3: Outline
Information theory basics
Shannon capacity
Modeling capacity of practical systems
Constellation constrained capacity
Proof of the Shannon Theorem

## Slide 4: What is Information Theory?
There are many ways to design communication systems
Two basic questions:
  How do we measure the performance?
  What is the best we can expect to do?
Information theory provides:
  Simple metrics to evaluate system performance
  Fundamental bounds that can be achieved by any system
  Apply to any communication system
  No constraint in computation / delay
Can be used as a benchmark for practical systems
Claude Shannon Founder of IT

## Slide 5: Entropy
Given a random variable
Entropy for a discrete :
Relative entropy for continuous with PDF :
Measures amount of “variation” in
  But, unlike does not depend on values of
  Just the number of values and their relative probability
Sometimes measured in “nats”
  Replace log base 2 with natural logarithm

## Slide 6: Discrete Examples
Ex 1: Binary
  See figure to the right
  Entropy maximized with most uncertainty,
Ex 2: Discrete uniform
  with
  Entropy increases with number of values
  Labels of the values do not matter

## Slide 7: Continuous Examples
Entropy increases with variance
Entropy does not change with mean
Distribution | Parameters | Relative Entropy in nats
Uniform |  | 
Real Gaussian |  | 
Complex Gaussian |  | 
Exponential |  | 
Distribution | Parameters | Relative Entropy in nats
Uniform |  | 
Real Gaussian |  | 
Complex Gaussian |  | 
Exponential |  | 

## Slide 8: Compression and Entropy
Key interpretation of entropy
number of bits to represent ”
  Related to the “compressibility” of
Specifically, consider variable length “encoder”:
  is a binary string
Want is “prefix” free
  is not a prefix of when
  Ensure mapping is invertible
  Given sequence of outputs, we can always tell boundaries
Raw data
Binary string

## Slide 9: Length of an Encoder
Given encoder
Define avg length of
Ex to the right: bits / sym
To minimize length:
  Select short sequences for likely
  Reserve long sequences for unlikely
Raw data
Binary string
A | 0.6 | 0
B | 0.3 | 10
C | 0.1 | 11
A | 0.6 | 0
B | 0.3 | 10
C | 0.1 | 11

## Slide 10: Compression and Entropy
Theorem: If is a discrete random variable, there exists a prefix free variable length code with
By encoding symbols at a time, can achieve
Proof uses a Huffman code
Entropy shows how much information is in a random variable

## Slide 11: Joint and Conditional Entropy
Let be a pair of discrete random variables with a joint distribution
Joint entropy: Entropy of the pair
Recall: For every is a distribution on
Conditional entropy for a given
  Represents entropy in after seeing
Conditional entropy:
Similar equations for continuous random variables

## Slide 12: Properties
Conditional:
Independence:
  if and only if and are independent
  In this case,
For all :

## Slide 13: Example
Suppose are binary with joint PMF in table
For
For
Conditional entropy:
 |  | 0.1 | 
 |  | 0.3 | 0.5
 |  | 0.4 | 
 |  | 0.1 | 
 |  | 0.3 | 0.5
 |  | 0.4 | 

## Slide 14: Mutual Information
How much are two random variables related?
Mutual information:
Represents decrease in entropy in from knowing
Can also define for differential entropy
Special cases:
  If and are independent,
  If , then

## Slide 15: Example: BSC Channel
For communications
  is the typ. the channel input and is the output
Binary symmetric channel:
  Input equiprobable
  Output
  Probability of error
  Probability no error
Mutual information
  bit
  Similarly,
  Hence:

## Slide 16: BSC Channel Illustrated
From
See vs. on right
When or 1
  perfectly describes
When
  and are independent

## Slide 17: Outline
Information theory basics
Shannon capacity
Modeling capacity of practical systems
Constellation constrained capacity
Proof of the Shannon Theorem

## Slide 18: Abstract Communication System
TX bits:
Maps bits to symbols into “channel”
Channel outputs RX symbols
Channel is modeled probabilistically
RX attempts to estimate TX bits:
TX
RX
Channel
Information bits
TX symbols
RX symbols
RX bits

## Slide 19: Practical System is an Example
TX
RX
Channel
Coding
Symbol
mapping
TX filtering
Decoding
Symbol
demod
RX filtering
In the abstract model, the TX and RX can include typical block we have studied up to now
But they are not restricted to a particular structure

## Slide 20: Key Parameters
Block length: number of symbols
Rate: number of bits per symbol
Block error rate:
  Depends on randomness in channel
Key goal in communication: maximize rate with a low BLER
TX
RX
Channel
Information bits
TX symbols
RX symbols
RX bits

## Slide 21: Discrete Memoryless Channel (DMC)
Model channel probabilistically via conditional distribution
  conditional distribution of the RX symbols given the TX symbols
Say channel is memoryless if
  Each RX symbol depends only on
For simplicity, we restrict to the discrete case:
  are finite sets
TX symbols
Channel
RX symbols

## Slide 22: Example Channels
Example 1: AWGN channel is memoryless
  Assume are independent
Example 2: BSC channel is memoryless and discrete
  TX and RX symbols are binary
  BSC channel is independent on each symbol
TX symbols
Channel
RX symbols

## Slide 23: Asymptotic Rate and Reliability
To obtain sharp results, we often look at the case of long block lengths
Formally, consider a sequence of TX-RX pairs as a function of the block length
For each
  number of information bits
  TX is some function:
  RX is some function:
Asymptotic rate:
Say it is asymptotically reliable if:
TX
RX
Channel

## Slide 24: Achievable Rate and Capacity
Achievable rate: We say a rate is achievable if:
  There exists a sequence of encoder-decoders indexed by block length with rate and
  The BLER vanishes:
Capacity: Is the supremum over all achievable rates
  Optimized over all possible encoders & decoders
  No regard to complexity or delay

## Slide 25: Shannon’s Capacity Theorem
Theorem: Given a DMC with transition the channel capacity is:
  We sketch the proof at the end of the lecture
Maximization is performed over distributions
With and , we can compute

## Slide 26: Example: BSC
Input output
Probability of error:
Can show that maximizing distribution is:
In this case, the mutual information is computed as before
  Capacity with higher capacity as

## Slide 27: AWGN Channel Capacity
Now suppose that
Although this channel is not discrete, similar theory applies using relative entropy
Limit input distributions such that where is a maximum energy per symbol
Theorem: The capacity of the AWGN channel with energy limit is:
Simple relation relating capacity to SNR

## Slide 28: Proof of AWGN Channel Capacity
AWGN channel:
First suppose that a Gaussian input
Entropy of complex Gaussian, is
Therefore
  Given
Hence
  Therefore, Gaussian input achieves the capacity
Can also show that for any distribution with
  Hence, any other distribution has lower

## Slide 29: Continuous Time Capacity
Consider continuous-time system:
  Assume and is bandlimited to bandwidth
  Noise is AWGN with PSD
Theorem: The capacity of the continuous-time AWGN system is:
  Most important formula in IT!
  Relates SNR, bandwidth and achievable rate
  Proof sketch in next slide

## Slide 30: Proof of Continuous-Time Capacity
We convert the continuous-time channel to a discrete-time channel
If is band-limited to , then there are degrees of freedom per second
So, we can find an orthonormal basis:
  The energy per symbol will be:
We can similarly write the received signal as where
Noise energy per symbol is
Capacity per symbol is
Since there are symbols / sec, the continuous-time capacity is

## Slide 31: Example
Suppose:
  TX power, dBm
  Path loss, dB
  Bandwidth, MHz
  Noise density (with noise figure) is dBm/Hz
Capacity:
  RX power, dBm
  SNR is dB
  In linear scale:
  Spectral efficiency is bps/Hz
  Capacity is Mbps

## Slide 32: Regimes
Two regimes
Power limited regime
  Suppose SNR is low
  Capacity is linear in power
  Bandwidth does not help
Bandwidth limited regime
  Suppose SNR is high
  Capacity is only logarithmic in SNR. SNR does not help much
  But grows much faster with bandwidth

## Slide 33: Practical Design Guidelines
Practical systems operate in a limited SNR range
Avoid very power limited regime
  Generally, keep dB
  Below this SNR, better to use smaller bandwidth and higher PSD
  Reduces overhead and computation
Avoid highly bandwidth limited regime
  Generally, keep to 30 dB
  Gains are very low with higher SNR
  Also, the gains are hard to achieve in practice
  In these cases, use more bandwidth

## Slide 34: SNR Per Bit and Spectral Efficiency
Shannon formula:
Spectral efficiency:
  Units are bits per second / Hz
  Represents rate / bandwidth
SNR per bit:
  Written as
  Pronounced “Ebb-noh”

## Slide 35: Outline
Information theory basics
Shannon capacity
Modeling capacity of practical systems
Constellation constrained capacity
Proof of the Shannon Theorem

## Slide 36: Problems Achieving Shannon Capacity
Shannon’s capacity formula is impossible to exactly achieve in practice
Achieving the capacity requires generating a “random codebook”:
Codebook requires entries
Grows exponentially with block length Prohibitive computation and memory
Also, introduces infinite delay
How close can we get to Shannon capacity in practice?

## Slide 37: Modulation and Coding Schemes
Practical systems use a modulation and coding scheme (MCS)
Coding:
  Ex: Convolutional, Turbo, …
  Defined by rate
Modulation via symbol mapping
  Typically, QAM
  Defined by bits / sym,
Spectral efficiency is:
Ex: 16-QAM with a Rate ¾ code
  bps/Hz
Channel coding
Symbol mapping
Coded bits
Info bits

## Slide 38: Measuring Gap to Shannon Capacity
Each MCS has a spectral efficiency (SE):
By Shannon Theory, we should achieve this SE at an SNR
Practical codes obtain a lower SE
We system operates below Shannon capacity
  Often quoted in dB:
Gap depends on the level of reliability (e.g., BLER) and implementation

## Slide 39: Example
Rate convolutional code with QPSK
Spectral efficiency achieved is:
SNR required for BER is dB
  See simulation to the right
Shannon theory:
  For in linear scale
  SNR per bit is in linear scale, 0 dB
Hence, we say this system operates 4.1 dB below Shannon

## Slide 40: Capacity and Bandwidth Loss
Most systems have loss to imperfect codes and bandwidth overhead
Simple model for achievable rate:
  fraction bandwidth overhead
  power loss
  = maximum spectral efficiency (due to max MCS)
Example:
  System operates 6 dB below capacity with a 20% bandwidth overhead and bps/Hz
  Bandwidth 20 MHz
  Suppose dB. In linear scale,
  Rate is: Mbps
  Shannon rate is Mbps

## Slide 41: Gaps to Shannon Theory for Early Codes
Shannon capacity formula and random codes, 1948.
  Determines the capacity
  But no practical code to achieve it.
Hamming (7,4) code, 1950
Reed-Solomon codes via polynomials over finite fields:
  Invented in 1960 at MIT Lincoln Labs
  Berlekamp-Massey decoding algorithm, 1969.
  Used in Voyager program, 1977. CD players, 1982.
Convolutional codes.
  Viterbi algorithm, 1969. Widely used in cellular systems. (Viterbi later invents CDMA and founds Qualcomm)
  Typically, within 4-5 dB of capacity

## Slide 42: Improvements with Modern Codes
1990s: major breakthrough via graphical models
Turbo codes (next class)
  Berrou, Glavieux, Thitimajshima, 1993.
  Able to achieve capacity within a fraction of dB.
  Adopted as standard in all cellular systems by the late 1990s.
LDPC codes
  Similar iterative technique as turbo codes.
  Re-discovered in 1996
  Used in 5G today
  Can provably hit Shannon capacity using graphs with spatial coupling, Richardson & Urbanke, 2012

## Slide 43: Outline
Information theory basics
Shannon capacity
Modeling capacity of practical systems
Constellation-constrained capacity
Proof of the Shannon Theorem

## Slide 44: Loss from Finite Constellations
Consider AWGN channel:
Theoretically optimal codebook is Gaussian
But, in practice, we use M-QAM or some discrete constellation for ease
Constellation-constrained capacity: Capacity given that must be in some given constellation
This section, we will show:
  How to define a constellation-constrained capacity
  How to compute a constellation-constrained capacity
  How to account for loss for sub-optimal bitwise decoding

## Slide 45: Capacity-Constrained Capacity Defined
AWGN channel:
With only constraint that capacity is:
  Optimal distribution is complex Gaussian
Now consider fixed constellation: with equiprobable symbols
  is the constellation (ex. M-QAM)
Define constellation-constrained capacity:
  Capacity for a fixed constellation

## Slide 46: Computing Capacity-Constrained Constellation
AWGN channel: with
Mutual can be computed numerically or via simulation easily:
  Since is equiprobable, number of bits / symbol
  Given , is Gaussian:
  Hence, by Bayes Rule:
  Therefore,
  Find
  Generate random pairs and obtain estimate

## Slide 47: Constellation-Constrained Capacity
Key insights:
Capacity with QAM saturates
Hence, high SNR requires large
Relative to Shannon Capacity
  Minimal loss at low SNRs (< 2 dB)
  Loss of 1-2 dB at high SNRs

## Slide 48: Bitwise LLRs
AWGN channel:
Up to now, we assume we decode each symbol
  Requires we find a PMF
  Finding this PMF is computationally expensive since number of bits / symbol
  Also, most decoders requires probabilities on bits not symbols
Practical systems decode each bit
  Suppose a mapping from bits to the symbol
  We then compute the bitwise LLR:
  This method is computationally simpler.
  But it is not optimal
What is the loss in capacity with bitwise LLRs?

## Slide 49: Binary Cross Entropy
Let unknown binary variable
Let : Estimate of the LLR
Define binary cross entropy
Measure of error: Large when:
  and large positive or
  and large negative
Commonly used in training binary classifiers
  See ML class

## Slide 50: BCE Mutual Information Bound
We derive a bound for a general binary input channel
TX: bit binary input bits and maps to a symbol vector
RX: Obtains any output and creates any vector
  Values can be the LLRs or any approximation of the LLRs of the bits
Theorem: The mutual information is bounded as:
  Proven at end of section
TX
RX
Channel

## Slide 51: LLR Mutual Information Bound
BCE bound can be used to find capacity with practical symbol demodulation
TX: Takes bits and creates QAM symbol with energy
Channel is
RX performs demodulation and creates LLRs
QAM mapping
LLRs
Channel

## Slide 52: QAM Capacity with Bitwise LLRs
Can compute the bound easily
Generate bits over symbols
Modulate to symbols
Add noise and get RX symbols
Compute LLRs
Compute MI:

## Slide 53: Bitwise Capacity
Each modulation is optimal in a range
  Select higher modulations at higher SNRs
At high SNRs:
  Need to select high modulation
Relative to Shannon Capacity
  Minimal loss at low SNRs (< 2 dB)
  Loss of 1-2 dB at high SNRs

## Slide 54: Bitwise vs Symbol-wise Decoding
Bitwise decoding has a small loss
But if correct constellation is chosen:
  Loss is small
  In most regimes, loss < 0.5 dB
Symbol-wise decoding
Bitwise decoding

## Slide 55: ML Perspective: Learn a RX from Data
Many modern designs train the RX from data
Represent RX as a function where represents parameters to train
  Ex: is a neural network and are the weights and biases
Can be useful when optimal receiver is difficult to derive or implement
  Non-coherent channel (when the channel must be estimated)
  Joint equalization and decoding
  Non-linearities
  Computational constraints
  Many possibilities…
TX
RX parameters
Channel

## Slide 56: Training a RX
BCE bound permits a simple procedure to train
  Generate samples .
  Each true bits transmitted
  RX will generate outputs: with outputs
  Adjust parameters to minimize BCE loss:
  Then mutual information is bounded above by:
TX
RX parameters
Channel

## Slide 57: BCE Bound Proof: Entropy Bound
To prove BCE bound, we need the following Lemma
Lemma: Suppose has some PMF and is any other distribution. Then
Equality holds when
Also applies to conditional distributions. If is any conditional distribution:

## Slide 58: Proof of Lemma
Let
Find to minimize s.t.
Lagrangian:
Take derivative:
Since
Hence the minimum is achieved at
Therefore, for all :

## Slide 59: Proof BCE Bound
Let true distribution on bits
Given define the conditional binary distribution:
Given , define the distribution on the bits as
  The bits are conditionally independent
Can verify that
Also
By Lemma:
Therefore:

## Slide 60: Outline
Information theory basics
Shannon capacity
Modeling capacity of practical systems
Constellation constrained capacity
Proof of the Shannon Theorem

## Slide 61: Proof: Achievability
First, we show that any is achievable
Use a random codebook!
Find a to maximize and select any
For each generate random messages or codewords:
  are iid
  Set of is called the message index
  Encoder maps bits to a message index and transmits
Each message is called a codeword
The set of messages is called the codebook:

## Slide 62: Joint Typicality
For large , we know (via the law of large numbers)
Say a vector is jointly typical if it satisfies the asymptotic values within some
Formally, we define the set of length sequences such that:

## Slide 63: Jointly Typical Decoder
Let be the set of codewords
Given receiver takes any from codebook such that
  That is, find such that is jointly typical
  If no such exists, or there is more than one, declare error
To analyze, suppose we transmit a true sequence and receive
We bound two errors:
  Type 1 Error: The correct codeword, , is not jointly typical
  Type 2 Error: There is another codeword, for some

## Slide 64: Type 1 Error
We use the following asymptotic equipartition property (AEP)
AEP 1: Let where are i.i.d. Then
Let be the true transmitted codeword
Then has components
Let = Probability Type 1 error = Probability that is not jointly typical
By AEP 1,

## Slide 65: Type 2 Error
For this error, we use the following AEP property
AEP 2: Let where are i.i.d. Then :
  In this case, for each and are drawn independent
Property shows with very high probability they will not be jointly typical

## Slide 66: Type 2 Error Continued
For some , let be the true transmitted codeword and the received symbols
Let = probability that there exists a codeword where
Since codewords are independent, has components
By AEP 2,
Since there are wrong codewords by union bound:
We know for some
Therefore, we can select such that

## Slide 67: Converse Proof
Must show that for any rate , is bounded away from zero
We will not cover this.
This is proved via Fano’s inequality
Take information theory class for more!