## Slide 1: Unit 7: Synchronization and Matched Filtering
EL-GY 6013: Digital communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Describe the synchronization mechanisms in common commercial standards
Formulate binary decision tasks as hypothesis testing problems
Compute the LRT detector for a hypothesis testing problem
Compute error probabilities and optimize the threshold
Formulate signal detection as a hypothesis test
Describe and analyze the matched filter detector
Analyze various non-idealities including clock offset, auto-correlation and multi-path
Simulate the MF detector for real systems

## Slide 3: This Unit
Channel coding
Symbol mapping
Coded bits
TX filter DAC
IQ symbols
Analog baseband
Upconversion
Info bits
Passband
Channel
Down-conversion
RX filter and ADC
Sync
Equalization
Symbol demod
Channel decoding
RF
“Noise”

## Slide 4: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection
Match Filtering Convolution
Automatic Gain Control (AGC)
Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 5: Synchronization and Detection Problem
Two key problems in most communication receivers:
  Detect if a transmitter is present
  Synchronize to the transmitter
Basic first step in any communication process
Assumes the transmitter broadcasts a signal
Receiver must detect and synchronize to it
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 6: Ex 1: 802.11g Transmission
All data is transmitted in frames
Frames may arrive at any time
Each frame begins with known preamble
  Common to all frames
RX station listens for preamble to detect:
  Presence of frame.
  If frame is present, determines timing delay of the remaining frame
Frame
PLCP header
MAC PDU
Preamble

## Slide 7: 802.11g PLCP Header Details
PLCP header details:
  Preamble: Used for initial detection, synchronization, channel estimation
  Rate: Signals MCS for service bits & MAC PDU
  Length: Number of OFDM symbols in frame
  Service: Scrambler sync
MAC header: Contains MAC layer control info
  Segmentation, MAC addresses, …
MAC FCS: frame check sum (used to detect errors)
Preamble
(16 us)
Rate
(4bits)
Length
(12 bits)
Service
(16 bits)
MAC header
PLCP header
Coded at lowest rate
Rate indicated in PLCP header
Payload
(MAC SDU)
MAC PDU
FCS

## Slide 8: Ex 2: LTE Downlink Primary Sync Signal (PSS)
Each cell transmits periodically PSS
  Narrowband, short (71.4 us x 1.08 MHz)
  One of 3 PSS signals
Once PSS is detected, mobile (UE) knows frame timing
  Decodes subsequent signals SSS, broadcast, …
Frequency

## Slide 9: Ex. 3. 5G New Radio Beam Sweeping
Directional synchronization for mmWave
Transmit multiple SS Burst
  One in each direction
MmWave typically use 120 kHz subcarrier spacing
With 120 kHz SCS:
  SSB = 4 OFDM symbols = 35.7 s
  Each SSB, contains a PSS
  PSS time duration = 1 OFDM symbol = 8.92 s
  Bandwidth = 127 SC = 15.24 MHz
  Up to 64 SS Bursts / burst period
  Typical SSB periodicity = 20 ms

## Slide 10: Simple Synchronization Model
TX sends a preamble / synchronization signal
  Complex baseband samples.
  Sample rate
If signal is present at RX:
  : Complex channel gain
  : Integer delay
Problem detect if signal is present or not.
  If so, what is the delay
For now, we assume:
  Integer delays, no multipath
  Will address these issues later
Delay=
TX
RX

## Slide 11: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection
Match Filtering Convolution
Automatic Gain Control (AGC)
Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 12: Hypothesis Testing
Classic problem in statistics or decision theory
Observe data
Two possible hypotheses for data
  H0: Null hypothesis
  H1: Alternate hypothesis
Model statistically:
  Assume some distribution for each hypothesis
  Each density is the likelihood of
Problem: Determine which hypothesis is true given data

## Slide 13: Applications
Many applications
Pattern recognition:
  Does this image contain a face or not?
  Is this person X?
Detection:
  Is the transmitted bit 0 or 1?
This lecture: Is a signal present or not?

## Slide 14: Simple Example
Scalar Gaussian
In this case:
Saw this earlier in BPSK transmissions
Max likelihood detector from earlier
  Selects the most likely hypothesis
  In this case

## Slide 15: Types of Errors
For binary detection problems, there are two errors:
  Type I error (False alarm): Decide H1 when H0
  Type II error (Missed detection): Decide H0 when H1
In many problems, the consequences of these errors is different
Example: Medical diagnosis
  False alarm: You tell the patient he is ill, when he is fine
  Missed detection: You miss the illness
  Consequences are different
Given detector, we define two error probabilities:
  False alarm probability:
  Missed detection probability:

## Slide 16: Likelihood Ratio Test
We can tradeoff the error probabilities with a likelihood ratio test:
Likelihood ratio test (LRT)
  is an adjustable threshold
  Increasing Lowers , but lowers
Often performed in log domain
Note that corresponds to maximum likelihood detector

## Slide 17: Gaussian Example
Scalar Gaussian case:
Log likelihood ratio:
LRT: if and only if
  is an adjustable threshold

## Slide 18: Computing Error Probabilities
From previous slide, LRT detector is:
FA probability:
  This is the area under the curve (blue)
  For Gaussian:
MD probability
  This is the area under the curve (orange)
  For Gaussian:

## Slide 19: Tradeoff
Tradeoff between and
Increasing threshold
  Decreases false alarms
  But increases missed detections
Selection of optimal threshold
  Depends on the application
  What are the relative costs of these errors?

## Slide 20: ROC Curve
Receiver operating characteristic
Plot of vs.
Trace out:
Random guessing achieves:
Higher the line is better

## Slide 21: Neyman-Pearson Theorem
Theorem: Suppose that an LRT obtains . Then any other test with will have a less than or equal to the LRT.
LRT is the most powerful test
Obtains best vs. performance

## Slide 22: In Class Exercise

## Slide 23: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection
Match Filtering Convolution
Automatic Gain Control (AGC)
Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 24: Simple Synchronization Model
TX sends a preamble / synchronization signal
  Complex baseband samples.
  Sample rate
If signal is present at RX:
  : Complex channel gain
  : Integer delay
Problem detect if signal is present or not.
  If so, what is the delay
For now, we assume:
  Integer delays, no multipath
  Will address these issues later
Delay=
TX
RX

## Slide 25: Detect as a Hypothesis Test
At each delay , we consider two hypotheses:
Signal is present:
  is a complex, baseband channel gain
  Recall that we are assuming a single path channel (for now)
Signal is absent:
In both cases, assume is white noise:
Delay=

## Slide 26: Hypothesis Test in Vector Form
Without loss of generality, consider delay
Let be the vector of RX samples:
Write two hypotheses in vector form:
  [Signal present]
  [Signal absent]
Geometrically:

## Slide 27: Match Filter Detector
Hypotheses:
  [Signal present]
  [Signal absent]
Match filter energy detector:
  Project RX signal to TX waveform
  Measure energy:
  Declare
  is a threshold
Later we will show this is the optimal hypothesis test

## Slide 28: False Alarm
False alarm
  Under
  Statistic
  This is a linear function of a Gaussian
  Hence,
  Hence is exponential with

## Slide 29: Missed Detection
Under
Statistic
Similar to FA calculation:
Can show:
  is a non-central chi squared with degrees of freedom
  Non-centrality parameter

## Slide 30: Simulation
Theoretically calculated threshold based on PFA target
Simulate PMD based on SNR

## Slide 31: Noise Estimation
Threshold
Requires we know noise energy
How do we estimate this?
Suppose
Consider residual signal:
  Component of not spanned by
  is the projection of onto an dim space
  Can show that
  Take noise estimate:

## Slide 32: Noise Estimation 2
Use threshold with estimate noise
Detector takes if
  But
  So test is equivalent to:
  Note fraction of energy in direction
Conclusion: With noise estimation MF is equivalent to

## Slide 33: In Class Exercise

## Slide 34: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection
Match Filtering Convolution
Automatic Gain Control (AGC)
Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 35: Match Filtering with Unknown Delay
Synchronization signal
RX signal at delay :
Problem: Detect if signal is present. If so, what is the delay ?
Match filter (without normalization) at delay is:
Hypothesis test:
  Detect signal at delay at

## Slide 36: Further Analysis Details
We need to examine three key practical issues that degrade performance
Preamble auto-correlation
Multi-path
Carrier offset

## Slide 37: Match Filtering as a Convolution
Match filter (without normalization) at delay is:
Define adjoint signal:
  Complex conjugate and time reversal
MF output can be computed via a convolution:
Filter with
Peak detection
Detected signal locations

## Slide 38: Signal Auto-Correlation
Consider what happens with no noise:
  , “True” delay
Run match filter:
Can show output is:
  autocorrelation of transmitted signal
Since we want small for we want: for
Many sequences with low auto-correlation
  Golay, Walsh, ….
Auto-correlation of Golay 128 sequence
Used in 802.11ad preamle

## Slide 39: Multipath
Up to now we have assumed that there is a single path:
But, in reality there is often multipath:
  Due to multi-path in channel and pulse shape filtering
Match filter has delayed copies of auto-correlation:
  One peak in MF output for each path
Ex: Two path channel
Path at
Path at

## Slide 40: Frequency Offsets
When initially searching for a preamble, there may be a significant carrier offset
Causes a phase rotation in samples:
  is the phase rotation per sample
  , frequency error, sampling rate
Must integrate over range where phase does not change significantly
  Pre-amble length must be
Example: Suppose the carrier offset =10 ppm, GHz and Gs/s
  samples
  In time duration, this is us
  A very short time before the signal is completely rotated

## Slide 41: Detailed Simulation Example
Transmit 128 length Golay pre-amble
Filter through channel with single (possibly fractional) delay
Set threshold for FA target of per 1000 samples
Measure MD probability as a function of the SNR
Filter with
Peak detection
Detected signal locations

## Slide 42: Calibration
Need to calibrate the FA probability and delay offset
Threshold
PFA
True Delay
Estimated Delay

## Slide 43: Missed Detection
Loss of about 3dB with fractional delay offset
Signal energy is split in two samples
Need to use over-sampling to compensate
  See lab

## Slide 44: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection
Match Filtering Convolution
Automatic Gain Control (AGC)
Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 45: Automatic Gain Control
AGC goal: Bring RX signal to “correct” level
Tradeoff of two factors
Want high gain: Overcome noise after AMP
But gain too high saturates RX
AGC finds optimal level
Variable gain AMP
Gain
control
RF front end
Digital baseband

## Slide 46: Mathematical Model
RF front-end
  Linear gain with noise:
  Noise after AMP
  Memoryless nonlinearity:
  and have PSD and
Digital baseband
  Measures RX power or SNR
  Controls gain
Variable gain AMP
Gain
control
RF front end
Digital baseband
+
+

## Slide 47: Analysis with No Nonlinearity
With no nonlinearity:
PSD of signal component in output:
PSD of noise in output:
Output SNR:
Variable gain AMP
+
+

## Slide 48: Analysis with No Nonlinearity Example
Output SNR from previous slide:
Fig to left: dB, dB
Observations with no nonlinearity:
  Increasing gain always improve output SNR
  Saturates at as
Design principle:
  Have high SNR (low noise) in first stage
  Increase gain to overcome noise in later stage
Typical RF design starts with a low noise amplifier (LNA)
Variable gain AMP
+
+

## Slide 49: Example with Saturation Nonlinearity
With high gain :
  Signal becomes large
  May saturate component distortion
Saturation occurs in many RF components
  E.g., mixer, LNA
Example:
  30 dB, 10 dB
  Nonlinearity is a saturation: Clips at
  Saturation level 50 dB
We see ideal gain trades off gain and NL distortion
+
+
Gain too high NL distortion
Gain too low Signal too small relative to
No NL
Ideal gain
With NL

## Slide 50: Example with ADC
Example ADC:
  Similar to quantization + saturation
  Saturates at with bits
With finite bit width
  Set gain to not overflow ADC
+
Gain too high NL distortion
Gain too low Signal too small relative to
Ideal gain
ADC

## Slide 51: Practical Gain Control
Measure RX power
  RX power over last symbols
Adjust gain:
  Decrease gain
  Increase gain
Threshold
  Set to ensure signal is not saturating
Variable gain AMP
Gain
control
RF front end
Digital baseband
+
+

## Slide 52: Gain Control in 802.11
WLAN systems require very fast AGCs
STF (short training field). Duration is s
  Used for detection and AGC
  Typically set AGC in first ~2
  Perform detection in remaining
Cannot detect STF until AGC has run
  Otherwise, signal will be too low in SNR or too distorted
AGC is implemented in hardware

## Slide 53: The 9361 Integrated Circuit
Gain performed in at least three stages
  LNA gain control at RF
  TIA (transimpedance AMP) gain at IF
  Digital gain during digital filtering
Single gain setting selects all three gains
  Ensure all intermediate points do not overflow
RX
TX

## Slide 54: AGC in the Pluto
MATLAB interface gain control
AGC Fast Attack
  AGC automatically performed in HW
  Ideal for WLAN with fast gain
  But host has no visibility to gain selected
Manual
  User can manually select gain
  We will use this in lab
  But it is very slow
  Just for education

## Slide 55: SDR Lab
https://github.com/sdrangan/sdrlab/tree/main/lab05_gain

## Slide 56: Outline
Detection and Synchronization Problem
Hypothesis Testing
Match Filtering for Detection
Match Filtering Convolution
Automatic Gain Control (AGC)
Matched Filtering as a Generalized Likelihood Ratio Test

## Slide 57: Likelihood Ratio Test
In vector form:
  [Signal present]
  [Signal absent]
Likelihoods:
  ,
  Cannot apply regular LRT since parameters are unknown
  GLRT

## Slide 58: Generalized Likelihood Ratio Test
Null hypothesis
Present hypothesis:
  Minimize over :
GLRT:
Details in clas