## Slide 1: Unit 8: Equalization
EL-GY 6013: Digital communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Describe the equalization problem
Implement and simulate a OFDM transmitter and receiver
Describe an OFDM channel
Implement a simple OFDM channel estimator via smoothing
Implement the symbol equalization
Simulate an end-to-end OFDM system

## Slide 3: This Unit
Channel coding
Symbol mapping
Coded bits
TX filter DAC
IQ symbols
Analog baseband
Upconversion
Info bits
Passband
Channel
Down-conversion
RX filter and ADC
Sync
Equalization
Symbol demod
Channel decoding
RF
“Noise”

## Slide 4: Outline
What is Equalization?
Time-Domain Equalization for Single Carrier Systems
OFDM
OFDM Channel Estimation, a preview…

## Slide 5: Multi-Path and ISI
Effective discrete-time channels often have many taps
Two causes:
  Multi-path: Physical channel has many paths (Reflections, scattering, …)
  Pulse shaping (TX and RX filter spread samples over time)
Causes inter-symbol interference (ISI):
  Each TX symbol received over many symbols
Multi-path indoor channel measured at UC Berkeley

## Slide 6: Equalization
Equalization: Any method to overcome ISI
This lecture we look at two main methods
Time-domain equalization
  Used in single carrier systems
Frequency-domain equalization
  Used in OFDM systems

## Slide 7: Linear Equalization
Discrete-time ISI channel:
Linear equalizers: Find a filter to approximately invert the channel:
In frequency-domain:
ISI channel
Equalization
h
g

## Slide 8: Training Symbols
All linear equalizers require training or reference signals
TX sends a known reference sequence
RX sees
Estimates channel and/or equalizer for
ISI channel
Equalizer estimator
h
TX reference
RX reference

## Slide 9: Outline
What is Equalization?
Time-Domain Equalization for Single Carrier Systems
OFDM
OFDM Channel Estimation, a preview…

## Slide 10: 802.11 ad Preamble for 60 GHz WiFi
STF: Short training field
  AGC, detection of packet
  coarse estimate of timing
  Process as previous lecture
CEF: Channel estimation field
  Train equalizer
  Apply equalizer

## Slide 11: 802.11ad Preamble Details
Based on complementary Golay codes
Have low auto-correlation
Gsamp/S
For data packets: STF = 1.23 s, CE= 0.654 s
Control packets
Longer STF.
Need to be decoded by all stations. No directional gain
Data packets
Shorter STF

## Slide 12: STF Detection
MF detector: Correlate with STF
  Gives good performance but expensive
Simpler delay detector

## Slide 13: Estimation from the CEF
Known sequence
Linear estimation problem

## Slide 14: Linear Estimation
We know:
Given in training field, but is unknown
Find a time-domain equalizer,
  Approximately inverts the channels
Simple LS equalizer
  Say we have reference symbols and want -tap equalizer
  Minimize least-squares cost
Will not discuss more in this class

## Slide 15: Outline
What is Equalization?
Time-Domain Equalization for Single Carrier Systems
OFDM
OFDM Channel Estimation, a preview…

## Slide 16: OFDM
Time-domain channel:
Time-domain equalization can be difficult
  When is over many samples, inverting channel is hard
OFDM Concept: Transmit in data in many narrowbands
  Divide bandwidth into “subcarriers” at frequencies:
  Transmit in parallel streams
  Each stream is band-limited: when outside
  If channel is flat in this band:
  This is a single tap channel!
  Easy to equalize

## Slide 17: History of OFDM
First proposed by Chang, Bell Labs,1966
Early applications in digital broadcast and DSL (for home Internet)
  Early digital TV, LER, Paris 1988
  ETSI Digital Audio Broadcast, 1995, ETSI Digital Video Broadcast, DVB-T, 1997, DSL, 1998
Wireless LANs:
  802.11a, 1999 and 802.11g, 2002
  802.11n, 2004 and many future standards (but not 802.11ad)
Cellular standards
  Early cellular standards Flash-OFDM, 2001 and WiMax, 2004
  LTE, adopted OFDM in 2005
  5G NR

## Slide 18: OFDM Symbol Structure in Time-Domain
Time is divided into OFDM symbols
  Each symbol divided into samples
  = sample rate
Each symbol has:
  FFT period, samples
  CP period, samples
  = number samples in FFT period
  = number samples in cyclic prefix
  samples per symbol
  symbol period
Cyclic prefix
FFT period
OFDM symbol
samples

## Slide 19: OFDM in Frequency Domain
Frequency is divided into subcarriers
  subcarriers
  Spaced at
Subcarriers are divided into:
  occupied subcarriers
  null subcarriers
Subcarrier frequencies:
  Digital frequency:
  Analog frequency
  Index

## Slide 20: OFDM Time-Frequency Grid
Data to be transmitted is an array:
  OFDM symbol index
  = subcarrier index
Resource element: One time-frequency point
TX data
  One complex value per RE
  Called a modulation symbol
Subcarrier space
OFDM symbol

## Slide 21: OFDM TX Modulation
Input: : Sequences of modulation symbols
Parallelize:
Insert null:
  location of occupied sub-carrier
IFFT:
Serialize with CP insertion:
  CP:
  FFT:
Modulation of OFDM symbols

## Slide 22: OFDM TX Modulation in MATLAB
Manually performing the operations
Using MATLAB’s built-in function
This is preferable and easier

## Slide 23: Multipath Channel
Now consider a multi-path channel:
  Assume for and
  That is, only for
Implicitly we have made two key assumptions
  Delay spread is less than samples = total length
  RX is aligned such that first path arrives at
TX OFDM symbol
Multipath channel
RX OFDM symbol

## Slide 24: Circular Convolution
Start FFT window after first path + CP period
  Start time=symbol time + first path + CP period
  Window of length
Assume delay spread
In each OFDM symbol, :
  Channel acts as a circular convolution
  (circular convolution over
  Circular due to CP
Delay for first arrival
TX OFDM
RX
]
TX symbol start

## Slide 25: Frequency Domain
Up to now:
In each OFDM symbol, :
  Channel acts as a circular convolution
  (circular convolution over
  Circular due to CP
Delay for first arrival
TX OFDM
RX
]
TX symbol start

## Slide 26: OFDM Receiver
Start FFT window after first path + CP period
  Start time=symbol time + first path + CP period
  Window of length
Assume delay spread
Then, there is no ISI
  RX window for symbol sees only TX symbol
Also, channels acts as a circular convolution:
Delay for first arrival
TX OFDM
RX
]
TX symbol start

## Slide 27: OFDM RX DeModulation
Find arrival of first sample of symbol 0
Take FFT window:
  Note the offsetting
FFT:
Remove un-unused SC:
  –th occupied subcarrier
Serialize:
DeMod of OFDM symbols

## Slide 28: OFDM Channel as Multiplication
Since channel is a circular convolution
  sampled digital frequency response
  Channel response may change with time
  Due to motion of TX, RX or scatters
Key result: OFDM channel is simple multiplication
Zero pad & IFFT
FFT & extract occupied sub-carriers
Circular convolution
RX symbols
Channel
TX symbols

## Slide 29: Degrees of Freedom and Overhead
Each OFDM symbol has DoF
Rate is:
Occupied bandwidth:
Fraction Overhead:
Cyclic prefix
FFT period
OFDM symbol

## Slide 30: CP Selection
Want CP small to make overhead low
Want CP large to ensure all paths fit in CP window
  Need CP > “delay spread”
  Delay spread tends to be larger in outdoor environments
Practical systems select CP to balance both objectives
Cyclic prefix
FFT period
OFDM symbol

## Slide 31: Ex: 802.11a/g OFDM
STF: For detection, AGC
2 OFDM symbols for initial channel estimate
4 pilots in remainder of symbols for tracking

## Slide 32: High Throughput 802.11n and 802.11ac
Increase bandwidth by using more subcarriers
Subcarrier spacing and CP length are identical

## Slide 33: 4G LTE
Bandwidth allocated in resource blocks
  1 RB = 12 subcarriers
15 kHz
FFT size up to:
Sample rate = = 30.72 MHz

## Slide 34: 5G NR OFDM
Flexible numerology
Supports different cell sizes and latency / granularity

## Slide 35: 5G NR OFDM Details
Subcarrier spacing: kHz
FFT size: Typically
Occupied subcarriers: DC
  number of “resource blocks”

## Slide 36: Outline
What is Equalization?
Time-Domain Equalization for Single Carrier Systems
OFDM
OFDM Channel Estimation, a preview…

## Slide 37: OFDM Channel Variations
OFDM Channel with Noise
Fading: Channels vary over time and frequency
  Due to interference between paths in channel
  Will discuss this more in wireless class
Variation in time:
  Due to Doppler spread,
Variation in frequency
  Due to delay spread
20 path random channel with Hz, ns
SNR [dB]

## Slide 38: Problems with Time-Varying Channels
OFDM Channel:
Problem 1: Channel Estimation
  Need to estimate channel
Problem 2: Equalization:
  Given , estimate data
We start with the equalization
20 path random channel with Hz, ns
SNR [dB]

## Slide 39: Symbol Equalization via Inversion
Consider a single time and frequency
Symbol equalization:
  Estimate from
  Also obtain a noise estimate (needed for LLR)
Channel inversion:
  Symbol estimate
  Noise estimate:
Symbol Equalization
+

## Slide 40: MMSE Symbol Equalization
Received noisy symbol:
MMSE estimation:
  Use linear estimate
  Select to minimize
Resulting estimate (shown with simple algebra):
  Estimate:
  Noise variance:
Provides lower noise estimate than channel inversion
Symbol Equalization
+

## Slide 41: Estimation Reference Symbols
Equalizers require training or reference signals
TX sends a known reference sequence on some locations
RX sees
Estimates channel and/or equalizer for
Fading channel
Equalizer estimator
h
TX reference
RX reference

## Slide 42: Ex: 5G NR RS
OFDM Channel
5G NR Demodulation Reference Signals
  Called DM-RS
  Transmitted in downlink with data (PDCSH)
  Very configurable in terms of over-head
Basic channel estimation idea
  Transmit know on DM-RS.
  Estimate on DM-RS symbols
  Interpolate to data symbols

## Slide 43: Example: 802.11 Channel Estimation
STF: Short training field
  AGC, detect packet, approximate timing
LTF: Long training field
  Estimate channel
Pilots in data
  Modify estimate to tracking time variations
  For 802.11, most variations are CFO

## Slide 44: Ex: LTE Pilots
Can average in time or frequency
Pilots (Cell Reference signals) in one RB

## Slide 45: Estimating Channel in a Single Symbol
First consider estimation in one symbol
True channel is
  sub-carrier index
RX:
DM-RS known
Example to right:
  10 MHz bandwidth
  200 ns delay spread
  10 dB SNR on DM-RS
Subcarrier

## Slide 46: Raw Channel Estimate
Channel:
On DM-RS positions, is known
Raw channel estimate:
  Can be computed in every DM-RS position
We see estimate is noisy

## Slide 47: Smoothing the Estimate
Raw channel estimates are:
  Noisy
  Only available on DM-RS locations
Often smooth the estimate
  Fit over all locations
Many options
  Linear interpolation, splines
  Parametric

## Slide 48: Lab and Beyond
Lab 6: You will:
  Build a simple smoothing estimate for an 802.11-like packet
  Measure SNR
In wireless class, you will learn a lot more:
  Fading and physical mechanisms for channel variation
  Kernel smoothing estimators
  Analysis of the estimators
  Bias-variance tradeoff